## Slide 1
✓
Configuration Audits
The functional and physical audits — what each one asks, which items get them, and what the teams actually check
Configuration Management · Overview Briefing
Notes: Overview briefing on configuration audits for a general audience: engineering, program management, quality, manufacturing, and leadership. Companion to the configuration items briefing.

## Slide 2
Two audits, two questions
Different evidence, different people, different moments. Neither covers the other's ground — which is why there are two.
Functional configuration audit
Does it do what it was required to do — and can you prove it?
Verifies tested performance against the approved functional and allocated documentation. Also confirms specifications and interfaces are adequately defined, and that the change control system genuinely controls release.
Works from test evidence against requirements.
Physical configuration audit
Is the thing you built the thing the documentation describes?
Examines the as-built — or as-coded — configuration of a validated item against its product documentation, confirming the documentation is a clear, complete and accurate representation of what was produced.
Works from the article against the released design.
What each cannot tell you. A design can be fully proven and the article in front of you still wrong. A unit can match its documentation perfectly and the documentation still describe something that does not meet its requirements.
Notes: Keep the two questions apart — nearly everything else follows from that. The bottom band is the point people miss: neither audit covers the other's ground.

## Slide 3
Why these audits are not optional
Some requirements arrive twice — through the contract, and through the safety management system, because they act as barriers to severe events.
2024
Door plug departs in flight
Installed without all four retention bolts. The as-built configuration diverged from the approved configuration and no record flagged it — every paper check agreed with every other paper check.
The physical examination is the step that is not reducible to a record.
2019–22
Tanker delivery escapes
Tools and debris repeatedly found in delivered aircraft, and repeated escapes between development, early production and full-rate production articles. Deliveries halted more than once.
Hence: identify the differences between the production unit and the functional audit unit.
2000
Wear strip, wrong material
A replacement thrust reverser strip made of titanium alloy rather than the specified stainless steel. It fell onto a runway; the resulting tyre debris ruptured a fuel tank. 113 fatalities.
Hence: material specification, to build record, to material certificate.
On safety-significant product lines these are performed regardless of what the contract flows down. A proposal not to perform one has three doors: perform it, replace it with a validated equivalent control, or accept the risk formally at the authority matching its severity. There is no fourth door.
Notes: Consequence first. The three anchors map to three specific audit requirements. Close on the floor gate: silent omission is the failure the gate exists to close.

## Slide 4
Only some items are audited
Two separate narrowings sit between everything in the product and everything that gets an audit. People collapse them constantly.
Everything in the product
Parts, materials, processes, software, documentation. All of it made, inspected and controlled. Most of it not separately managed.
Configuration items
Selected against the identification criteria. Each carries its own documentation, identifier, baselines and change control. A program may have hundreds.
Designated for audit
A much smaller subset again, chosen by the designation assessment. A program with hundreds of configuration items may audit a handful.
“It is a configuration item, so it will be audited.” No. Most configuration items are never audited, and nothing is wrong with that.
“It is not audited, so it is not really controlled.” Also no. Being a configuration item is what confers documentation, identifiers, baselines and change control.
Notes: The funnel answers the first question every audience asks: are we auditing everything? Both errors at the bottom come from treating one selection as if it were the other.

## Slide 5
How an item earns an audit
Four parts, completed at initial audit planning, at every plan revision, and on any trigger. Recorded for every item evaluated — designated or not.
PART A
Mandatory
Named in the contract, statement of work or plan? An item the customer controls and whose product baseline they will establish?
Any yes designates — then keep going. Contract scope is a floor, not a ceiling.
PART B
Safety criticality
Hosts a hazard risk control? Failure could cause serious injury or loss of primary capability? Top two severity bands? Safety-critical software or firmware? Single point of failure?
Any yes creates presumptive designation. Omission needs documented System Safety concurrence.
PART C
Risk factors
New or novel design · substantive change since last audit · new source, process, facility or tooling · new sub-tier supplier · escape history · work not to approved data · reconciliation anomalies · never audited
Two or more designate. Exactly one is recorded and monitored.
PART D
Reassessment triggers
Design, process, facility, tooling or supplier change · escape or safety event · reconciliation anomaly · hazard log revision adding a control · plan revision
Re-run the assessment. A program accumulates triggers for years.
Every answer has a source — the hazard log, quality and safety data, procurement records, reconciliation indicators. A “no” that means nobody checked is indistinguishable on the form from one somebody established.
Notes: Part A does not end the assessment. Part C's single-factor rule matters: one factor is recorded so the second lands on top of a documented one.

## Slide 6
Order, and what has to be true first
Each prerequisite is structural rather than administrative — the audit has nothing to work on without it.
1
Approved baselines
Functional and allocated documentation approved by the customer. Without it you audit against a draft that moves underneath the finding.
→
2
Functional audit
Tested performance against approved requirements. Produces the validated item.
→
3
Physical audit
Examines the as-built configuration of a validated item. Cannot precede validation.
→
4
Product baseline
Established by the customer on successful completion and specification approval. Every later change is formal change action.
Before the physical audit convenes, on the specific unit
Build records closed
Every work order closed and every non-conformance dispositioned and closed. Until they are, the as-built configuration is not final and the reconciliation is provisional.
Unit jointly selected
Early production-representative, serial numbers identified. A unit chosen by the party being audited is an exhibit, not a sample.
Access, wherever it sits
To the floor, the tooling and the instructions actually used. Embodiment is not a barrier: access extends to the installed item and its zone.
Notes: The order is not convention: the physical audit examines a validated item, and validation is what the functional audit produces.

## Slide 7
The functional audit: walking the chain
For every requirement, or an agreed sample, the audit walks one documentation flow from end to end.
Baseline requirement
→
Test plan
→
Test procedure
→
Test report
Or the analysis, inspection or demonstration record standing in place of a test — an empty cell reads as an unverified requirement, and at the audit it will be treated as one.
Open with what failed
The design-team briefing has a required slot for requirements not met, with proposed remedies. A briefing that reaches it with nothing to say has either an unusually clean program or a briefing problem — and the audit establishes which.
Sampling has one hard limit
Where sampling is agreed, requirements verifying hazard risk controls and other safety-critical requirements are in the sample. They are not sampled out — and this is the rule a compressed schedule attacks first.
Tell the truth about what is open
Where verification depends on integrated testing not yet performed, partial completion is acknowledged, open requirements become action items, and a delta audit closes them once the testing passes.
For a software item the standard is stated flatly: every requirement has a related test step, and that test passes. Not most requirements — and not the requirements that were testable within the schedule.
Notes: The traceability matrix is what converts the audit from a meeting into evidence: anyone can pull a requirement two years later and walk the chain.

## Slide 8
The physical audit: what is actually checked
Matching part numbers establishes identity. Every other check exists because identity is not conformity.
The article against its data
Product definition data alignment, at the governing revision
Approved changes and flight changes incorporated
Approval, clearance and qualification of installed part types
Certification and plan status
Form, fit, interface and workmanship
Nameplate, marking and unique identification
Installed software load, version and checksum
The article against its records
Serial, lot and heat numbers — article, requirement and record
Life-limited items: limit and life consumed at delivery
As-designed child items in the closed build records
Material and process conformance, in three links
Traceability upward to the next higher assembly
Foreign object debris in the embodied zone
Records against records
Build traveler, buy-off and calibration status
Manufacturing instructions against the sampled design data
Non-conformance and variance adjudication
Sub-supplier end item inspection and test
Spares released before the audit
Differences from the functional audit unit, certified
Each check states what is compared against what, what evidence is acceptable, and what a finding looks like. Sampling sizes belong to the audit plan — with one fixed exception: features implementing or protecting hazard risk controls are never sampled out.
Notes: This is the check set, grouped by what is being compared. The opening line is the whole argument: part number matching is an identity check, not a conformity check.

## Slide 9
Each defect is caught by exactly one check
One unit, three defects. Every defect passed most of the check set — which is the argument for the whole of it, made without appealing to thoroughness.
A washer stack and lockwire on the as-designed data have no entry in the closed work orders. The joint looks complete.
Part numbers agree · workmanship passes · traveler stamped
Found by
Child item reconciliation
The unit was built to a work instruction written against a superseded revision. The revision did not change the part number. Every operation is stamped.
Data alignment passes · buy-off passes · nothing raised as a non-conformance
Found by
Instructions against design data
A bracket's heat number on the article matches the heat number on the as-built record. The certificate for that heat is for a different alloy.
Traceability passes — correctly. The numbers do agree.
Found by
Material and process conformance
A shortened check set is not a faster audit. It is a different audit, with defined blind spots. Note the third row: numbers matching numbers is the failure the set exists to break, reappearing inside a single check.
Notes: Worked example. The third defect is the uncomfortable one: the traceability check was performed correctly and still did not help.

## Slide 10
The system-level audit is not an audit of everything
Where audits run in increments, a final system-level audit confirms the system baseline is correct. It has two populations — and neither is the drawing set.
Child items not yet audited
Swept against the designation criteria. Items that now designate are audited as items, with their own entry criteria, data package and lead time. A program accumulates triggers for years, so an item that failed designation at award may pass comfortably by the time the system is complete.
Interfaces between items
Verified against their interface control documents at a common effectivity, with both sides' as-built compared to the definition. Each item's own audit verified its side against its own data. No item-level audit establishes that two items meet correctly.
The installation drawing set is not the audit population. It is the means of locating what to examine. A sample drawn from drawings rather than from items and interfaces is mis-scoped regardless of the percentage — it concentrates in structure and wiring by drawing volume, while no designated item is audited at all.
Baseline coherence. Open items from earlier increments closed, and effectivity consistent across items audited years apart — two audits can each be correct and describe configurations never approved to sit in the same aircraft. Timing. Run the sweep at the plan revision before the capstone, not at its door: a newly designating item needs its own lead time.
Notes: The misreading is expensive in both directions — auditing the whole bill of materials, or sampling drawings. Both end with no designated item audited.

## Slide 11
Findings, and what the audit produces
The checks are not the deliverable. What survives the audit is the record it leaves behind.
Major or minor follows the mechanism
Not the instance count. One instance produced by a systematic breakdown is major — that mechanism will produce more. Fifty independent transcription slips are fifty slips. When you cannot tell, ask what would have had to work for this not to happen, and whether that thing is working.
Nine outputs, not four
Findings, documented and provided to the customer
Action items — issue, plan, owner, suspense date
Minutes, carrying evidence as well as proceedings
Records that findings have been rectified
A summary report of what was found
A detailed report — only after verified closure
An invitation to witness anything re-accomplished
A final system-level audit where increments were used
The product baseline itself
Two reports, sequenced
The first states what was found. The second is prepared only after the customer verifies the completed items, and states what was verifiably closed. A single report issued on claimed closure collapses the distinction that matters.
Minutes as an evidence package
The drawings package with its manufacturing instructions, completed inspection reports, baseline records including spares released before the audit, sub-supplier confirmations, and the parts selection list — all provided within the minutes.
There is no verbal finding
A discrepancy both sides discussed and nobody wrote down did not happen, and will be re-argued as though it never did. Daily minutes are reviewed jointly at the start of the next session, for exactly that reason.
Notes: The nine outputs are what the standard requires. The three cards are the ones teams most often get wrong.

## Slide 12
What to remember
An audit is a discrete validation of the machinery that runs continuously — not a substitute for it, and not a re-inspection of one article.
1
The functional audit asks whether the design was proven. The physical audit asks whether this unit is that design. Neither covers the other's ground.
2
Being a configuration item decides what is managed separately; designation decides which of those get an audit. Two selections, two records.
3
Prerequisites are structural: approved baselines before the functional audit, validation before the physical one, and closed build records before either examines a unit.
4
Matching part numbers establishes identity, not conformity — and each defect in practice is caught by exactly one check, which is the argument for the whole set.
5
The system-level audit is scoped to items not yet audited and to interfaces between them. Drawings locate what to examine; they are not what is examined.
6
Findings classify by mechanism rather than count, and a finding is a measurement of the process — a repeat finding two years later is telling you about the organisation, not the item.
Notes: Close on the audit as a check on the verification system. If a systematic finding does not change how the process runs, the next audit finds it again.