## Slide 1
SAFETY MANAGEMENT · CONFIGURATION MANAGEMENT
Ground Rules & Assumptions as Configuration-Controlled Safety Artifacts
Closing the gap between inherited GR&A, SM-0001 safety risk management, and EIA-649-1 configuration control — across hardware, human factors, and interfaces.
Prepared for: Enterprise SMS Technical Fellow
Discussion draft — proposed practice, not current standard text
Notes: Framing: this is a bridge between two mature control systems we already run — the SMS/SRM stack under SM-0001 and the CM stack under EIA-649-1. Neither standard mandates a GR&A register today. The proposal is to make GR&A a first-class controlled artifact so that assumption validity is re-examined by mechanism rather than by memory.

## Slide 2
THE PRACTICE TODAY
Programs inherit GR&A on the basis of similarity
WHEN
Initial GR&A are written at proposal — several lifecycle states before configuration items exist and before any hazard analysis has been performed.
WHY
Rebuilding GR&A is expensive. The cost of rebuilding lands on the bid; the consequence of not rebuilding lands on execution, years later. The incentive is structural, not cultural.
WHAT TRANSFERS
The GR&A statement and its conclusion. Rarely the conditions that made it true on the donor program, and almost never the evidence that those conditions still hold.
Similarity of hardware is a claim about one item. A GR&A is a claim about that item inside a specific operating environment, installation, duty cycle, maintenance program, and organization.
The GR&A that matter most are written by the people who best understand why — and read years later by people who cannot reconstruct that reasoning.
Notes: Do not present this as a discipline failure. It is an incentive failure. Any fix that relies on bid teams voluntarily spending more will not hold.

## Slide 3
FAILURE MODE
The conclusion travels. The conditions stay behind.
What a GR&A actually is
A conditional risk-control credit:
"this risk is acceptable PROVIDED X is true."
What hardware similarity establishes
At most one of the X's — and only the ones expressed as part-level attributes.
Conditions that do not travel with a part number
Installation & mounting
Duty cycle
Thermal / vibration environment
Inspection interval & detectability
Operator and maintainer behaviour
Interfacing systems
Staffing & training level
Fleet utilisation
SM-0001 lists assumptions as a hazard-log field precisely so they can be re-examined when they change. Reuse-by-similarity copies an assumption into a state where nobody knows what a change would look like.

## Slide 4
THE ONE THAT IS A COMPLIANCE FINDING
Second failure: risk acceptance with no accountable person
1
The donor program accepted a risk
Someone named, on another program, under another risk-tolerability envelope, accepted the residual risk that the GR&A left open.
2
The receiving program inherits the credit
The statement arrives. The acceptance decision does not — there is no named acceptor on the receiving program, and no record that one was asked.
3
The assumption becomes background truth
Unbound and unowned, it stops reading as a decision at all. By CDR it is simply how the program understands the product.
SM-0001 requires risk acceptability criteria to be defined and responsibility for accepting risk to be clearly assigned.
A provisional GR&A still carrying risk credit at CDR is therefore a live noncompliance — not a schedule item. Framing it that way is what gets it funded.
Notes: This is the slide that converts the topic from good engineering hygiene into an SMS compliance obligation. Lead with it when talking to program leadership.

## Slide 5
EXISTING OBLIGATIONS, NOT NEW ONES
SM-0001 already gives us the hook
Assumptions are a hazard-log field
Appendix 2 lists assumptions among hazard-record content, with the stated rationale that they can be examined when they change to see whether the risk assessment still holds.
System description bounds scope
The organizational system description documents which areas are subject to SRM — so it also bounds which GR&A must be controlled, and lets us defend excluding the rest.
Risk acceptance must be owned
Acceptability criteria and the responsibility for accepting risk must be clearly defined; the Accountable Executive owns tolerability and can stop work at unacceptable risk.
Human & organizational factors
Risk controls must take operational, technical, human and organizational factors into account — which places human-factors GR&A squarely inside the SMS, not beside it.
We are not asking for a new requirement. We are asking that an existing hazard-record field be given an owner, a lifecycle, and a configuration anchor.

## Slide 6
WHAT NEEDS TO HAPPEN
The record: what a controlled GR&A carries
Identity
Unique ID · owner · binding state
Statement
The assertion, kept separate from its rationale
Rationale
Why it was made — the part that is impossible to reconstruct later
Validity conditions
Falsifiable claims about what must be true for the statement to hold
Configuration anchor
CI, baseline and revision each condition depends on — cited, never restated
Consuming analyses
FHA / FMEA / SSA / task analysis / compliance finding
Dependent hazards & controls
Which hazard and which risk control lose their basis if this fails
Named risk acceptor
The person on THIS program who accepts the residual risk
Inheritance provenance
Donor program, donor GR&A ID and revision, basis of the similarity claim
This is SM-0001's own hazard-record data model — scope, owner, risk-control responsibility, assumptions — reused one level down.

## Slide 7
GR&A ↔ CI
Configuration items work in both directions
↓
Downward — dependency
The GR&A cites the configuration documentation that makes it true, rather than restating it. Restating is how assumptions go stale silently. This converts "these programs are similar" from a judgement into a CI-to-CI comparison against baselined product configuration information.
↑
Upward — scoping
EIA-649-1 3.2.1(2)(b) already designates as a CI any item whose failure could cause serious injury, loss of life, or loss of primary capability. GEIA-HB-649 Appendix D adds criteria 5 and 10b. That safety-significant CI set is a defensible boundary for which GR&A get floor treatment.
Change management is the actual re-examination trigger
If GR&A cite CI baselines, configuration status accounting answers "which GR&A depend on this CI at this revision" — and an engineering change against that CI mechanically surfaces every downstream assumption, hazard and risk control. Existing obligations do the work: 3.3.1.2 (safety-affecting changes are Class I), 3.3.1.4(1) (ECP data must support evaluation of full impacts), 3.4.1(3)(a) (CSA keyed by CI identifier).
Adding a GR&A-impact field to the ECP form is a form change, not a new process. That is the single cheapest intervention in this deck.

## Slide 8
THE TIMING PROBLEM
GR&A are born years before configuration items exist
GR&A are at their most consequential and least verifiable at proposal — exactly when reuse-by-similarity is most tempting and configuration evidence is thinnest.
Proposal
GR&A created
Concept
Functional baseline
Development
Allocated baseline
Detail design
CI identification
Verification
Product baseline
In service
Field evidence
Assumptions live here, unverified and unowned
The wrong answer
"Start controlling GR&A at CI identification." That arrives years after the damage is done and after the assumptions have hardened into background truth.
The answer: progressive binding
Create GR&A early and unanchored, then bind them to successively firmer configuration artifacts as baselines emerge — tracking the residual unbound set as explicit debt.

## Slide 9
PROGRESSIVE BINDING
Bind to baselines, not to CIs
CI selection is explicitly iterative — top-level candidates emerge during concept and program definition, lower tiers follow. You do not need a CI set to start binding.
PROVISIONAL
Proposal
Recorded with owner, rationale and falsifiable validity conditions. No configuration anchor exists.
BOUND — FUNCTIONAL
Functional baseline
Performance envelope and operating environment GR&A bind. Many proposal GR&A discharge or reopen here.
BOUND — ALLOCATED
Allocated baseline
Interface, installation, thermal, loads and duty-cycle GR&A bind. Human-factors GR&A bind to procedure and training baselines.
BOUND — CI
CI identification / CDR
Bound to specific CIs and revisions. First point at which "similar hardware" can be checked rather than asserted.
VERIFIED
Product baseline / FCA-PCA
Validity conditions confirmed by test, audit or analysis. Falsification becomes a Class I change.
What matters is that the provisional population is visible and shrinking, and that named gates require its reduction.

## Slide 10
NO BASELINES EXIST — THIS STATE IS PURE PREVENTION OF LATER BLINDNESS
State 0 · Proposal & pre-award
Action / Requirement | Owning activity | Anchor
Create a GR&A record for every assumption that carries risk credit: ID, owner, statement, rationale | Program Mgmt · SE | New GR&A register
State validity conditions as falsifiable claims about the eventual product and its environment | Systems Engineering | GR&A record
Record inheritance provenance: donor program, GR&A ID, revision, asserted basis of similarity | Systems Engineering | GR&A record
Capture the donor program hazards and risk controls the reused GR&A were serving — seed hazard set | SRM | SM-0001 §6.2.1
Flag every GR&A provisional; stand up provisional-count as a metric from day one | SMS (Safety Assurance) | SM-0001 §6.3.2
Separately tag GR&A with no part number — human-factors and organizational assumptions | Human Factors | GR&A register
Budget and scope the GR&A discharge work in later states before bid submittal | Program Management | Program plan / basis of estimate
Define the GR&A identifier convention and control class in the draft CM Plan | Configuration Mgmt | CMP · EIA-649-1 3.1

## Slide 11
FIRST REAL HAZARD IDENTIFICATION; FIRST REAL BINDING
State 1 · Concept & material solution → functional baseline
Action / Requirement | Owning activity | Anchor
Perform system-level hazard identification and test each provisional GR&A: does it carry risk credit? | SRM | SM-0001 §6.2.1
Scoping decision — only risk-bearing GR&A enter the controlled floor; the rest stay engineering notes | SMS + SRM | System description
Assign a named risk acceptor to every risk-bearing GR&A; inherited acceptance is void by default | SMS (Accountable Exec) | SM-0001 §6.2.2
Document the organizational system description — it bounds which GR&A are in SMS scope | SMS | SM-0001 §6.2.2
Bind performance-envelope and operating-environment GR&A to the functional baseline | Systems Engineering | FCD · EIA-649-1 3.2.3
Nominate top-level CI candidates using safety-criticality criteria; concur with acquirer | Config Mgmt + SE | EIA-649-1 3.2.1(2)(b)
Establish GR&A as a controlled data type in the engineering release system | Configuration Mgmt | CMP · EIA-649-1 3.2.2

## Slide 12
WHERE INHERITED-ASSUMPTION FAILURE CONCENTRATES
State 2 · Development → allocated baseline
Action / Requirement | Owning activity | Anchor
Decompose hazard analysis to subsystem; restate GR&A validity conditions at that level | SRM | SM-0001 §6.2.1
Bind interface, installation, thermal, loads and duty-cycle GR&A to allocated baseline documentation | Systems Engineering | ACD · EIA-649-1 3.2.3
Identify internal and external interface requirements; incorporate into FCD/ACD; place under control | Configuration Mgmt | EIA-649-1 3.2.5.1
Nominate lower-tier safety-significant CIs; each pulls its dependent GR&A into floor scope | Config Mgmt + SE | GEIA-HB-649 App. D
Bind human-factors GR&A to procedure, training-curriculum and manual baselines | Human Factors | Procedural baselines
Begin provisional-GR&A burndown reporting against named gate criteria | SMS (Safety Assurance) | SM-0001 §6.3.2
Flow GR&A ownership and reporting obligations to suppliers through contract and interface documents | Supply Chain + CM | SM-0001 §7.5

## Slide 13
THE GATE WHERE SIMILARITY IS FINALLY CHECKABLE
State 3 · Detail design → CDR
Action / Requirement | Owning activity | Anchor
Bind remaining GR&A to specific CIs and revisions — cite configuration documentation, never restate it | Systems Eng + CM | Product config information
Run the delta assessment for every inherited GR&A: donor CI vs recipient CI, plus environment delta | Systems Eng + SRM | GR&A register
Conditions that cannot be verified against recipient configuration data reopen into SRM — no transfer | SRM | SM-0001 §6.2.1
Risk assessment against defined acceptability criteria; residual provisional GR&A raised as noncompliance | SMS | SM-0001 §6.2.2
Add a GR&A-impact field to the ECP form and wire the GR&A↔CI link into change impact assessment | Configuration Mgmt | EIA-649-1 3.3.1.4(1)
Verify CSA can answer: which GR&A depend on this CI at this revision? | Configuration Mgmt | EIA-649-1 3.4.1(3)(a)
Validate operator and maintainer assumptions against draft procedures and task analysis | Human Factors | Task analysis
Hold the CDR gate criterion: provisional GR&A count at or below the agreed threshold | Program Management | SETR criteria

## Slide 14
EVIDENCE REPLACES ASSERTION
State 4 · Verification, FCA / PCA & certification
Action / Requirement | Owning activity | Anchor
Move GR&A binding state from bound to verified as test and analysis evidence accrues | Systems Engineering | GR&A register
Extend requirements-to-test traceability through to the GR&A that scoped each requirement | Systems Eng + Quality | EIA-649-1 3.5.2.1(1)(c)
Process any GR&A falsified by test as a Class I (major) change | Configuration Mgmt | EIA-649-1 3.3.1.2
Conduct FCA and PCA; document non-compliances; reconcile production vs development CI differences | Config Mgmt + Quality | EIA-649-1 3.5.2 / 3.5.3
Validate the risk controls that depended on GR&A; confirm effectiveness measures are in place | SRM + SMS | SM-0001 §6.3.1
Confirm assumed task times, detectability and workload by test or simulation rather than assertion | Human Factors | HF validation plan

## Slide 15
KEEPING THE LINK ALIVE THROUGH CHANGE VOLUME
State 5 · Production
Action / Requirement | Owning activity | Anchor
Screen every engineering change proposal for GR&A impact | Configuration Mgmt | EIA-649-1 3.3.1.4(1)
Reopen the affected GR&A whenever a recurring variance is converted to permanent | Config Mgmt + SRM | EIA-649-1 3.3.2(2)
Monitor whether GR&A re-validation is actually happening on change, or being waived | SMS (Safety Assurance) | SM-0001 §6.3.2
Maintain CSA by CI identifier; perform as-designed to as-built reconciliation | Configuration Mgmt | EIA-649-1 3.4.1
Treat repeat nonconformances as candidate invalid manufacturing or human-factors GR&A | Quality + Human Factors | SM-0001 §6.2.1
Trigger HF GR&A review on procedure or training revision even where no hardware ECP exists | Human Factors + CM | Procedural baselines

## Slide 16
THE LOOP CLOSES — AND REOPENS FOR THE NEXT PROGRAM
State 6 · In service, continued airworthiness & reuse export
Action / Requirement | Owning activity | Anchor
Route continued-operational-safety findings to GR&A owners, not only to hazard owners | SRM | SM-0001 §6.3.1
Re-validate GR&A on schedule and on trigger; track assumption age as an indicator | SMS (Safety Assurance) | SM-0001 §6.3.3
Confirm retrofit incorporation matches the configuration the GR&A assumed | Configuration Mgmt | EIA-649-1 3.4.1(6)
Use historical configuration traceability to scope which units a falsified GR&A affects | Configuration Mgmt | EIA-649-1 3.4.1(3)(b)
Export GR&A with validity conditions, configuration references and verification evidence attached | Program Mgmt + SE | GR&A register
Prohibit export of bare GR&A statements — that is what reproduces the original failure | SMS | Enterprise policy

## Slide 17
OWNERSHIP SUMMARY
Who owns what
Program Management
Funds and schedules GR&A discharge; owns gate criteria and the provisional-debt position; owns export discipline on derivative bids.
Systems Engineering
Writes validity conditions; performs binding and the delta assessment; owns the GR&A-to-configuration citation.
Configuration Mgmt
Makes GR&A a controlled data type; owns the CI link, the CSA query surface, the ECP impact field, and interface control.
SRM
Determines which GR&A carry risk credit; reopens unverifiable assumptions; routes in-service findings back to GR&A owners.
SMS / Safety Assurance
Owns scope via the system description, the named-risk-acceptor rule, burndown monitoring, and periodic re-validation.
Human Factors
Owns the GR&A class with no part number; binds to procedural and training baselines; validates task, workload and detectability claims.
Quality, Supply Chain and Training carry supporting actions at States 2, 4 and 5. No activity owns this end-to-end today — that is the gap.

## Slide 18
BEYOND HARDWARE
Human factors: the GR&A class with no part number
A hardware similarity review is structurally silent on these. They have no part number, so nothing in the CI comparison surfaces them — yet they are the most reused GR&A we hold.
Assumed training and certification level · crew workload · maintainer skill mix · inspection detectability · time available to complete a task · alert salience and annunciation · staffing levels · shift and fatigue patterns · assumed compliance with procedure
Where their validity lives
Not in configuration documentation. In the operating environment — personnel, procedures, facilities, training — which SM-0001 already treats as part of the system description.
What to anchor them to
Procedure, training-curriculum, task-analysis and manual baselines. EIA-649 already treats operation and maintenance manuals as derived from configuration documentation; extend control to the ones that carry risk credit.
The gap that lets them rot
A procedure or curriculum revision generates no hardware ECP. Nothing triggers re-examination. Close it by making procedural baseline changes a GR&A review trigger in their own right.
The disguised case
FMEA detectability ratings are human-performance assumptions wearing hardware clothing. So are assumed inspection intervals. Reuse them and you have silently reused another program's workforce.

## Slide 19
BEYOND HARDWARE
Interfaces: same box, different context
Reuse-by-similarity is a claim about the item. An interface GR&A is a claim about the item's context — which is precisely what did not travel.
Technical interfaces (CI ↔ CI)
Already obligated: identify internal and external interface requirements, incorporate them into the FCD/ACD/PCD, and maintain configuration control of the baselined requirements (3.2.5.1); provide an ICWG representative where one exists (3.2.5.2). Bind interface GR&A to these artifacts.
Organizational interfaces (org ↔ org)
SM-0001 §7. The classic failure: the supplier assumed the integrator covered it; the integrator assumed the supplier had. The assumption falls into the gap between two SMSs, each of which believes the other owns it. Name the GR&A owner per interface in the interface documentation (§7.5).
One caution on §7.4
SM-0001 rightly limits the propagation of hazard and risk analyses across interfaces to avoid unnecessary noise. That must not be read as licence to withhold interface GR&A. The assumptions that cross an organizational boundary are the minimum necessary exchange — they are exactly the content §7.4 was written to protect, not to suppress.
Interface GR&A are where inherited-assumption failure concentrates: the hardware is genuinely the same, and everything it touches is different.

## Slide 20
SYNTHESIS
Three classes of GR&A, three anchors
Hardware & performance
Anchors to
CI and product configuration information
Systems Engineering + CM
Binds at allocated baseline through CDR; verified at FCA/PCA.
Human factors & organizational
Anchors to
System description plus procedure, training and manual baselines
Human Factors + SMS
Binds at allocated baseline; revalidated on every procedural or curriculum change.
Interfaces
Anchors to
ICD / FCD / ACD plus interface agreements and contracts
CM + Supply Chain
Binds at allocated baseline; owner named per interface in interface documentation.
A GR&A with no anchor in any of the three is not an assumption. It is a hope with a document number.

## Slide 21
WHAT I AM ASKING FOR
Five decisions
1
Adopt GR&A as a controlled data type
Named in the enterprise CM Plan, with an identifier convention, a control class and a CSA field. CM owns the mechanism.
2
Require a named risk acceptor per risk-bearing GR&A
Inherited acceptance void by default. SMS owns the rule; this is the compliance-relevant item.
3
Add a GR&A-impact field to the ECP form
Cheapest intervention in the deck. A form change, not a new process.
4
Make provisional-GR&A count a reported gate criterion
At SRR, PDR and CDR. Program Management owns the position; Safety Assurance owns the metric.
5
Prohibit export of bare GR&A statements to derivative programs
Validity conditions, configuration references and verification evidence travel or nothing does.
Two honest caveats
Neither SM-0001 nor EIA-649-1 mandates a GR&A register — this is a bridge we are constructing, so it should carry the same Clean / Judgment / Conditional annotation as the CM Floor Register. And applied broadly it is expensive: scope it to GR&A a hazard analysis or compliance finding actually depends on, and defend that scoping through the system description.
Notes: Close on the incentive point: the cost of rebuilding GR&A lands on the bid, the consequence of not rebuilding lands on execution. Process alone will not hold this. It needs an accountable owner spanning both — which points at the Safety Accountable Executive.