## Slide 1
Configuration Items
What they are, how they are chosen, and why the choice carries the weight of the whole configuration management system
Configuration Management · Overview Briefing
Notes: Overview briefing on configuration items for a general audience: engineering, program management, quality, and leadership.

## Slide 2
What a configuration item is
Any hardware, software, firmware — or aggregation of them — that satisfies a system end-use function and is designated for separate configuration management.
The key word is designated: being a CI is a decision, not a property of the part.
Designation buys four things
An item that is not a CI has none of these in its own right — it is controlled only inside its parent’s documentation. For most items, that is exactly right.
Separate requirements
A specification of its own — performance stated and owned at its level.
Separate verification
Its performance is proven against those requirements, on the record.
Separate change addressability
Changes are proposed, evaluated, and approved against it by identity.
Separate status visibility
Its configuration is known — as designed, as built, as maintained — at any time.
Notes: Definition per the national consensus standard family. Emphasize: designation is a decision with consequences, not a label.

## Slide 3
Why the decision matters
Every selection decision is a decision about which items get the machinery.
Not separately auditable
No audit walks its requirements to test evidence, and no physical audit examines its as-built truth.
Not separately change-controlled
Modifications to it are never proposed or approved against it — they simply happen inside a parent’s drawing package.
Invisible in status accounting
Nobody can answer “what configuration is it in?” — because no record is kept at its level.
For most items that is acceptable. For a safety-critical item, it means the thing whose failure could kill someone sits outside every barrier the CM system provides — which is why safety-critical selection is treated as non-negotiable regardless of what a contract flows down.
Notes: The three cards state what non-designation means. Close on the safety floor concept without citing internal document numbers.

## Slide 4
How items are selected
STEP 1
The end-use function gate
Does the item satisfy a system end-use function?
Fails the gate: raw materials, bulk commodities, structural elements with no defined functional role. These are controlled inside their parent’s documentation — not designated.
Software passes essentially always — and is essentially always designated.
STEP 2
The selection criteria — one or more designates the item
a
Critical to the functioning of the system
b
Failure could cause serious injury, loss of life, or loss of primary capability
c
Complex, not well known, critical to program goals
d
Under control as designated by the customer
e
Needs separate type designation, versions, or nomenclature
f
Critical or high risk with significant financial impact of failure
g
Requires logistics elements — provisioning, manuals, test equipment, maintenance
Criterion (b) is the safety-critical criterion — applied on safety-significant product lines regardless of contract flow-down, and every candidate gets a documented rationale, designated or not.
Notes: Two-step screen. Highlight criterion (b) as the safety anchor. Documented rationale for every candidate is what makes the screen auditable.

## Slide 5
Not everything should be a CI
Selection level is chosen for acquisition and support together — the level at which items are specified, contracted, accepted, and supported.
Too many CIs
Every minor revision becomes formal change traffic. Board agendas swell, cycle times stretch — and the real failure appears: engineers route around the process.
The cost is not paperwork. It is workarounds.
The right set
Items are designated where they are separately specified, verified, released, or supported — and not below. Changes address the item that changed.
The test is a sentence, the judgment is the job.
Too few CIs
Replaceable units have no identity to provision against. Software cannot release on its own cadence. Changes to one thing are changes to everything.
Visibility and control are lost exactly where things change.
Notes: The three-column consequence framing. Over-designation breeds workarounds; under-designation loses control where change happens.

## Slide 6
A CI is not a part number
A CI is a functional designation; a part number is a design identity. The two map to each other — but not one-to-one.
Same part, different functions
One part number
Command-link antenna CI
Telemetry antenna CI
Two installations, each with its own requirements and its own verification → two CIs sharing one part number. Merging them leaves one function without addressable requirements.
Same function, variant builds
One CI
Part no. -001 (units 1–12)
Part no. -002 (units 13 on)
A non-interchangeable detail (a connector change) separates part numbers, not CIs. The variant mapping lives in the CI index — and each variant’s interface callout is its own interface record.
Notes: The two recurring puzzles and their opposite resolutions. Antenna case and connector-variant case.

## Slide 7
Structure mirrors the architecture
System
Flight control
Propulsion
Computer
Software
Controller
Firmware
One decomposition, two views: the CI hierarchy and the architecture model are not allowed to diverge.
Mirror rule
Where a model-based architecture exists, CI parent-child structure mirrors its decomposition — each CI cross-referenced to its model element, each element carrying its CI identity.
Divergence hold
A CI decision that disagrees with the model is held until the model is dispositioned. Recording against a divergent model creates two truths — the disease CM exists to prevent.
Control boundary
Customer-controlled CIs are distinguished from internally controlled levels; below the customer’s line, the company decides what to manage and how.
Notes: Tree graphic on the left; three rules on the right. The mirror rule and the never-record-against-a-divergent-model discipline.

## Slide 8
Interfaces live at CI boundaries
The CI structure defines a finite set of boundaries — every pair of interfacing siblings, every external system, every customer/internal control line. That finiteness is what makes interface coverage checkable.
Engineering identifies
What crosses each boundary — signals, loads, data, power — is systems engineering work. CM does not derive interface requirements.
CM records and verifies coverage
Every boundary appears in the interface register with either defining documentation or an explicit, signed no-interface determination. No boundary is left blank — and coverage, unlike content, is checkable without engineering judgment.
Baselines protect
Interface requirements enter the configuration documentation as it develops; once baselined, they change only by formal change action.
Caution: appearing on the same interface document is not evidence of a common interface — one document can define several distinct interfaces.
Notes: Division of labor on interfaces and the coverage-not-content principle. Middle card carries the CM role emphasis.

## Slide 9
Identifiers carry the history
Assignment is convention; retention is the discipline. Three rules carry safety weight:
Part numbers change on non-interchangeability
A modification that breaks interchangeability changes the part number — that is the signal the number exists to send. The design identity moves with the design.
Unit identifiers never change
Serial, lot, and batch numbers are never revised or re-used. A modified unit keeps its serial through the part-number change — the serial is the thread its whole history hangs on.
Life survives everything
A life-limited part’s consumed life carries through modification and overhaul, exactly as its serial number does. Resetting it is a safety event, not bookkeeping.
Plus: software versions get distinct identifiers whenever build equivalence is not guaranteed, and part numbers are unique only within a design activity’s enterprise code.
Notes: The three retention rules, framed as the safety-bearing subset of identifier practice.

## Slide 10
Baselines anchor the lifecycle
Functional baseline
System-level performance requirements and their verification — typically at the system requirements/functional review.
Allocated baseline
Performance requirements allocated to each CI — typically at preliminary design review for the item. Interface requirements ride in the invoking specifications.
Product baseline
The complete released design description and acceptance requirements — established through the physical configuration audit; every change thereafter is formal change action.
A baseline plus its approved changes is the current approved configuration — the reference point every change, audit, and status record addresses.
Notes: Timeline of the three baselines with the audit tie for the product baseline.

## Slide 11
Identification is never finished
The CI set you shipped at the design review is a snapshot. The process owns keeping it true — re-running the screen and the structure alignment on triggers:
Design change
New items, new functions, new interfaces — or a variant that breaks interchangeability.
Model change
The architecture decomposition moves; the CI structure re-aligns with it.
New hazard finding
Hazard analysis identifies a safety-critical item — it gets screened, and will almost always designate.
Support strategy shift
An item becomes separately provisioned or separately repaired — the logistics criterion re-fires.
Contract change
The customer directs designation or de-designation; concurrence is iterative, not one-time.
New supplier
The one programs forget: a source change is itself a risk trigger across the CM system.
Notes: Six re-identification triggers; the new-supplier card is highlighted because it is the one most often missed.

## Slide 12
What to remember
1
A CI is a decision, and the decision selects which items get requirements, verification, change control, and status visibility of their own.
2
The screen is two steps — the end-use function gate, then the criteria — with a documented rationale for every candidate, kept honest by restraint.
3
Level matters as much as membership: designate where items are separately specified, verified, released, or supported, and not below.
4
Part numbers and CIs map many-to-many; structure mirrors the architecture model; boundaries are covered or explicitly determined empty — never blank.
5
Serial numbers and consumed life outlive every modification; that permanence is a safety barrier, not an administrative habit.
6
Safety-critical designation is the floor: it holds regardless of what a contract flows down, and identification re-runs whenever the facts move.
Notes: Six takeaways; end on the safety floor and the living-process point.