## Slide 1
SAFETY MANAGEMENT · CONFIGURATION MANAGEMENT
Making Ground Rules and Assumptions Traceable, Owned, and Re-checkable
Programs today inherit ground rules and assumptions from earlier programs when the hardware looks similar. This deck explains why that quietly breaks safety risk management, what to do about it, at which point in the lifecycle, and who owns each action.
Prepared for the Enterprise SMS Technical Fellow
Discussion draft. Configuration management terms are explained in plain language on slides 10 to 12, and a glossary is at the back.

## Slide 2
START HERE
The whole argument on one page
1. What we do today
When a new program reuses hardware from an earlier program, it also reuses that program's ground rules and assumptions. The assumption text is copied across. The reasoning behind it, and the conditions that had to be true for it to hold, usually are not.
2. Why that is a safety problem
An assumption is not a fact. It is a promise that a risk is acceptable so long as certain things stay true. Copy the promise without the conditions and nobody downstream can tell when it has stopped being true.
3. Why programs do it anyway
Rebuilding an assumption set costs senior engineering time during the most schedule-compressed part of a program. The cost is immediate and visible; the risk it creates is deferred and invisible. Reuse is the rational local choice.
4. What we are proposing
Not that programs stop reusing. That they reuse in a form that can be checked: each safety-relevant assumption written down with its conditions, tied to a controlled engineering document, and given an owner on the receiving program.
The key idea
The mechanism already exists. Configuration management already tracks which engineering documents changed and what depends on them. If assumptions point at those documents, then a change to the hardware automatically raises the question of whether the assumption still holds. Today nothing raises that question.
Slides 3 to 8 set out the problem. Slides 10 to 12 explain the configuration management terms. Slides 13 to 17 set out the fix. Slides 19 to 25 give the actions state by state, with the owning activity for each.

## Slide 3
DEFINITIONS
What a ground rule or assumption actually is
In safety work, an assumption is rarely a neutral statement about the world. It is almost always a conditional claim that lets an analysis stop somewhere. It says: this risk does not need further treatment, because something else is taking care of it.
The shape of a safety-relevant assumption
"This hazard is acceptable WITHOUT additional design mitigation, PROVIDED that (a) the flight crew is alerted within one flight, (b) the line is inspected every 400 flight hours, and (c) the unit is installed outside the icing-exposed bay."
The claim
The part everyone reads and repeats. "No additional mitigation required." It is short, quotable, and travels easily between programs.
The conditions
Items (a), (b) and (c). These are what make the claim true. They are longer, less memorable, and are the first thing lost in a copy-paste.
The risk credit
Because of this assumption, a hazard was closed without a design change. That is a real safety decision, and someone had to accept it.
This is not a new idea
SM-0001 already treats assumptions this way. Appendix 2 lists assumptions among the things a hazard record should contain, and the stated reason is so that they can be re-examined when they change, to see whether the risk assessment still stands. The standard therefore assumes we know when an assumption has changed. Today, for inherited assumptions, we usually do not.

## Slide 4
RUNNING EXAMPLE
A worked example we will carry through the deck
A pressure sensor unit is qualified and in service on Program A, a transport aircraft. Program B is a derivative and reuses the same unit, same part number, same supplier. The bid team carries across Program A's assumption set on the basis that the hardware is identical.
Program A · where the assumption was written
Alerting
Crew alerting logic detects a blocked line within one flight and annunciates it.
Procedure
Crew procedure requires the aircraft be dispatched under a specific MEL condition.
Inspection
The line is inspected every 400 flight hours under the approved maintenance program.
Installation
The unit sits in a heated bay, outside the icing-exposed zone.
Conclusion
Undetected blockage need not be addressed by design. Hazard closed.
Program B · what is actually different
Alerting
Different avionics supplier. The alerting logic exists but the detection threshold is not the same.
Procedure
Different operator, different MEL, and a crew procedure that was rewritten.
Inspection
The customer's maintenance program uses a 600 flight-hour interval.
Installation
The bay layout changed. The unit is now closer to the icing-exposed zone.
Result
The part number is genuinely identical. Every condition the assumption relied on has moved.
Nobody did anything wrong here. Each of those four changes was made by a different team, for a good reason, at a different time. No single person ever saw all four together next to the assumption they invalidate.

## Slide 5
THE PRESSURE THAT DRIVES THIS
Why programs reuse assumptions, and when that is right
This is not a discipline problem and it should not be presented as one. Reuse of ground rules and assumptions is a rational response to real pressure, and in most cases it produces the correct answer. Any proposal that ignores that will be rejected, and should be.
The schedule pressure is real
Assumption sets are written during proposal and early design, which is the most compressed part of any program. Rebuilding one from first principles costs weeks of senior engineering time that the bid does not have.
The incentives point one way
The cost of rebuilding lands on the bid, now, and is visible to everyone. The risk created by not rebuilding lands on execution or on the fleet, years later, and is visible to nobody. Every individual decision to reuse is locally sensible.
Reuse is usually correct
When the part, the installation, the operating environment, the customer and the maintenance program are genuinely the same, the earlier assumption still holds and rebuilding it wastes money. Most reuse falls in this category.
So the problem is not reuse
The problem is reuse in a form that cannot be checked. If the conditions are not written down and not tied to anything, then when one of them changes there is no way for anyone to find out.
What we are actually asking for
We are not asking programs to slow down. We are asking that the fast path leave a trace. Writing down the conditions attached to an assumption at the moment it is made costs minutes, because the person writing it already knows them. Reconstructing those same conditions three years later costs weeks, and often cannot be done at all. The expensive version of this work is the one we do today.

## Slide 6
WHAT GOES WRONG
The conclusion travels. The conditions stay behind.
When an assumption is copied to a new program, what physically moves is the sentence. The reasoning that produced it lives in the head of the engineer who wrote it, in a review that happened years ago, and in documents belonging to the other program.
What arrives on the new program
"Undetected blockage need not be addressed by design."
One sentence. Reviewed, approved, and now part of how the new program understands the product.
What stays behind on the old program
The alerting threshold. The MEL condition. The 400-hour interval. The bay location. The name of the person who accepted the residual risk, and the risk tolerability rules they were working to.
Similarity of hardware answers only one of these questions
How and where it is installed
How hard it is worked (duty cycle)
Temperature, vibration, icing exposure
How often it is inspected, and by whom
What the crew is alerted to, and when
What it is connected to on this aircraft
How the operator actually flies it
What the maintenance program requires
A part number is a claim about one box. An assumption is a claim about that box inside a whole aircraft, a whole operation and a whole organization.

## Slide 7
RISK ACCEPTANCE WITH NO OWNER
The part that is a compliance finding, not just bad practice
Behind every assumption that closes a hazard, there is a person who accepted the residual risk. When the assumption is inherited, that acceptance does not come with it, and no equivalent decision is made on the receiving program.
1
Someone on the earlier program accepted a risk
A named individual, working to that program's risk tolerability rules and its definition of acceptable risk, decided the residual risk was acceptable given the assumption held.
2
The new program inherits the benefit but not the decision
The sentence arrives and closes the same hazard again. But nobody on the new program was asked to accept anything, and there is no record showing that the question was put to anyone.
3
Within a year or two it stops reading as a decision at all
Unbound and unowned, the assumption becomes background truth. By critical design review it is simply part of how the program describes the product, and challenging it feels like challenging a fact.
Why this is the slide to lead with in front of program leadership
SM-0001 requires that the level of risk the organization is willing to accept be defined, and that responsibility for accepting risks be clearly assigned. An inherited assumption that is still carrying risk credit at critical design review, with nobody named against it, does not meet that requirement. That framing matters: it turns this from a good-practice suggestion into something a program has to resource.

## Slide 8
THE ECONOMICS
What it costs to find out late
The argument against doing this work is that it costs time we do not have. That argument only holds if you compare the cost of validating an assumption against zero, rather than against the cost of validating it later.
Proposal
Write the conditions down while you still know them
Minutes per assumption. The engineer making it already has the reasoning in their head.
Preliminary design
Check the assumption against the emerging design
Hours to days. Analysis is revisited, but nothing has been committed.
Critical design review
Discover the assumption does not hold
Weeks to months. Design change, rework, requalification of affected analyses.
Certification
Discover it during compliance demonstration
Months. Re-analysis, possible retest, a schedule slip visible to the customer and the authority.
In service
Discover it from field evidence
Fleet action. Service bulletin, inspection campaign, possible airworthiness directive.
The cheapest point in the whole lifecycle to capture an assumption is the one point where we currently capture nothing. Note that the cost figures above are illustrative of the shape of the curve, not measured across our programs.

## Slide 9
SECTION TWO
Configuration management, in plain language
The next three slides explain the configuration management concepts this proposal relies on. If you already work with configuration items and baselines, skip to slide 13. If you do not, these three slides are the ones that make the rest of the deck make sense.

## Slide 10
PRIMER 1 OF 3
Five terms, and why each one matters here
Configuration management is the discipline that keeps track of what the product is supposed to be, what it actually is, and what changed. It is already running on every program. We are proposing to hang assumptions off it rather than build anything new.
Configuration item
A part of the product that is important enough to be managed and tracked in its own right, with its own identifier, its own documents and its own change control. Not every bracket is one. The engine controller is.
Configuration documentation
The set of approved drawings, specifications and requirements that define what a configuration item is supposed to be. This is the authoritative record. If it is not in here, it is not controlled.
Baseline
An approved snapshot of that documentation at a point in time. Changes after that point have to go through formal review. Programs set several baselines as the design matures.
Engineering change proposal
The formal package used to propose a change to something already baselined. It has to describe the change and the full extent of its effects before anyone approves it.
Configuration status accounting
The record-keeping function that can answer questions like "what is the current approved definition of this item" and "what changes are outstanding against it". It is, in effect, a searchable index of the product.
Why this matters for assumptions
Configuration status accounting is the only system on the program that already knows what changed and what depends on it. If assumptions point at configuration items, that system can tell us which assumptions a change puts at risk.

## Slide 11
PRIMER 2 OF 3
What makes something a configuration item
Configuration items are chosen, not discovered. A program decides which parts of the product warrant individual tracking, because tracking everything at that level would be unaffordable. The relevant point for us is what the selection criteria already say.
The criterion that already does our work for us
EIA-649-1 says an item should be designated a configuration item if its failure could cause serious injury, loss of life, or loss of primary mission capability. GEIA-HB-649 adds similar criteria covering safety of personnel and equipment. In other words: the standards already single out the safety-significant items and require that they be individually identified and change-controlled.
This gives us a defensible boundary
We do not have to invent a rule for which assumptions get formal treatment. The items whose failure matters for safety are already flagged by the configuration item selection process. Assumptions that carry risk credit for those items are the ones we control.
It also keeps the scope affordable
The alternative, controlling every assumption on the program, is not affordable and would not survive contact with a bid. Tying scope to the safety-significant configuration item set is both cheaper and easier to defend to an auditor.
Selection is iterative, not a single event
Top-level configuration items are nominated early, during concept and program definition. Lower-tier ones follow as the design decomposes. This matters because it means we do not have to wait for a complete list before we start.
Interfaces are covered too
The standards separately require internal and external interface requirements to be identified, written into the controlled documentation and kept under change control. That is where most inherited assumptions actually fail.
Plain version: the safety-critical items are already on a list, and that list is already maintained. We are proposing to attach assumptions to it.

## Slide 12
PRIMER 3 OF 3
Baselines: the timeline an assumption can attach to
A program does not go from nothing to a full drawing set overnight. It fixes the definition in stages. Each stage gives an assumption something firmer to point at, which is what lets us start controlling assumptions long before configuration items are settled.
Functional baseline
What the system has to do
The approved system-level specification. Performance, operating envelope, top-level interfaces.
WHAT BINDS HERE
Assumptions about the operating environment and performance envelope can bind here.
Allocated baseline
What each part has to do
Requirements pushed down to subsystems and items, including the interfaces between them.
WHAT BINDS HERE
Interface, installation, thermal, loads and duty-cycle assumptions bind here. So do most human-factors ones.
Product baseline
What it actually is
The detailed design definition: drawings, part numbers, the as-built configuration.
WHAT BINDS HERE
Assumptions bind to specific items at specific revisions, and can be verified by test and audit.
This is the answer to the obvious objection. Assumptions are written at proposal, and configuration items do not exist for years. But baselines arrive in stages, and each stage gives us something to attach to. We do not wait. We bind progressively, and we keep count of what is still unattached.

## Slide 13
WHAT WE ARE PROPOSING
The fix, in one page
Write the conditions down, at the moment the assumption is made
Every safety-relevant assumption gets a short record: what is being assumed, why, and specifically what has to be true for it to hold. Written by the person who knows, when they know it. This is the cheap step and it is the one that unlocks everything else.
Point each condition at a controlled document rather than restating it
If the assumption depends on a 400-hour inspection interval, it cites the document that sets the interval instead of repeating the number. Restating is how assumptions quietly go stale when the source changes.
Give every risk-bearing assumption a named owner on this program
Someone here accepts the residual risk. Inherited acceptance from the earlier program does not count. This is the item SM-0001 already requires and it is the one with compliance teeth.
Let the change process raise the question automatically
Once assumptions point at controlled documents, an engineering change against one of those documents surfaces every assumption that depends on it. Nobody has to remember. The mechanism does the remembering.
Bind progressively, and count what is still unbound
Assumptions start unattached at proposal and attach to firmer documents as baselines arrive. What matters is that the unattached population is visible, reported at design reviews, and shrinking.
Do not inherit. Re-baseline.
An assumption cannot be carried across as-is. It can be re-adopted after a documented comparison of the two programs covering the conditions, not just the part number. Anything unverifiable goes back into safety risk management.
Five of these six are record-keeping and routing. Only the sixth costs real engineering time, and only for the small set of assumptions that actually carry risk credit.

## Slide 14
THE ARTIFACT
What goes in the record
This is deliberately close to the hazard record content that SM-0001 Appendix 2 already asks for. We are reusing a data model the safety organization already understands, applied one level down.
Identifier and owner
A unique number, the engineer responsible, and the current binding state.
The assumption itself
The claim, stated on its own, separate from the reasoning behind it.
The reasoning
Why it was made. This is the part that becomes impossible to reconstruct after a few years, and the part most worth capturing.
The conditions
What has to be true. Written so that someone could check them and get a clear yes or no.
What it points at
The controlled document, item and revision each condition depends on. Cited, not copied.
What depends on it
Which analyses use it, and which hazard would reopen if it turned out to be false.
Who accepted the risk
The named individual on this program. Not the person on the earlier program.
Where it came from
If inherited: the source program, the original record number and revision, and what the similarity claim was based on.
None of this is exotic. Most programs already hold four of these eight fields somewhere. The gap is that they are held in a document nobody queries, rather than a record something can trigger off.

## Slide 15
THE SINGLE MOST IMPORTANT HABIT
Cite the document. Do not restate the number.
This looks like a trivial formatting preference. It is the difference between an assumption that can be checked automatically and one that cannot.
Restated · goes stale silently
"Assumes the line is inspected every 400 flight hours."
When the maintenance program moves to 600 hours, nothing connects that change to this sentence. The sentence stays in the document, still reading as true, for the life of the program.
Cited · breaks loudly when it should
"Assumes the inspection interval defined in [maintenance requirement document, item, revision]."
When that document is revised, the change record shows this assumption among the things affected, and someone is required to say whether it still holds.
Why the citation is what makes the mechanism work
Under EIA-649-1, an engineering change proposal has to describe the full extent of a change's effects before it is approved, and safety-affecting changes are classified as major. If assumptions cite controlled documents, they show up inside that existing assessment. If they restate values, they are invisible to it.
Cheapest single intervention in this deck: add one field to the engineering change proposal form asking which assumptions are affected. That is a form change, not a new process, and it converts assumption review from something people have to remember into something the workflow asks for.

## Slide 16
HOW IT WORKS OVER TIME
Binding an assumption, stage by stage
Each assumption carries a state showing how firmly it is attached. The state is what gets reported at design reviews. The goal is not perfection, it is that the unattached population is known and falling.
UNATTACHED
Proposal
Recorded with an owner, the reasoning and the conditions. Nothing to point at yet, because no baseline exists. This is where every assumption starts and it is fine to be here at this stage.
ATTACHED · SYSTEM LEVEL
Functional baseline
Operating environment and performance assumptions now point at the approved system specification. A meaningful proportion of proposal assumptions get discharged or reopened here.
ATTACHED · SUBSYSTEM LEVEL
Allocated baseline
Interface, installation, thermal and duty-cycle assumptions attach. Human-factors assumptions attach to procedure and training documents rather than to hardware.
ATTACHED · ITEM LEVEL
Detail design and CDR
Pointing at specific items at specific revisions. This is the first moment at which "the hardware is similar" can actually be checked instead of asserted.
VERIFIED
Product baseline and audits
The conditions have been confirmed by test, analysis or audit. From here on, anything that falsifies the assumption is handled as a major change.
Expect the count of unattached assumptions to be uncomfortable the first time a program reports it. That is the point of measuring it.

## Slide 17
KEEPING THIS AFFORDABLE
Not every assumption gets the same treatment
If this applies to every assumption on a program it will be rejected, and rightly. The scope decision is made once, early, and it is what determines whether the practice survives contact with a schedule.
TIER 1
Controlled
Assumptions a hazard analysis or a certification finding actually depends on. Full record, pointed at controlled documents, named risk acceptor, reported at design reviews.
IN PRACTICE
Expect a small minority of the total. On most programs this is tens of items, not hundreds.
TIER 2
Registered
Assumptions that shape design decisions but carry no safety risk credit. Identifier, owner, statement and reasoning captured. No document citation required, no gate reporting.
IN PRACTICE
Cheap to maintain. Its value is that a Tier 2 item can be promoted to Tier 1 later if analysis shows it is load-bearing.
TIER 3
Engineering note
Everything else. Working assumptions, estimating conventions, modeling simplifications with no safety consequence.
IN PRACTICE
No control at all. Explicitly saying so is what makes Tier 1 credible rather than diluted.
Tier 1 scope is bounded by the organizational system description that SM-0001 already requires, and by the safety-significant items the configuration item selection process already identifies. Both are existing artifacts, so the boundary is defensible to an auditor without inventing a new rule.

## Slide 18
SECTION THREE
What happens when, and who owns it
Seven lifecycle states. For each one: the actions required, the activity that owns each action, and the existing document or standard clause it hangs off. Owning activities are shown as Program Management, Systems Engineering, Configuration Management, SRM, SMS Safety Assurance, Human Factors, Quality and Supply Chain.

## Slide 19
NO BASELINES EXIST YET, SO EVERYTHING HERE IS ABOUT LEAVING A TRACE
State 0 · Proposal and pre-award
Nothing can be attached to anything at this point, and that is expected. What this state has to produce is a written record of what is being assumed and why, made by the people who still know the answer. Everything later in the deck depends on this state being done properly.
Action required | Who owns it | Hangs off
Create a short record for every assumption that closes or reduces a hazard: number, owner, claim, reasoning | Program Mgmt with Systems Eng | New assumption register
Write the conditions as things somebody could later check and get a yes or no answer to | Systems Engineering | Assumption record
If the assumption came from an earlier program, record which one, which record, which revision, and what the similarity claim rested on | Systems Engineering | Assumption record
Capture the hazards and risk controls the borrowed assumptions were serving on the source program | SRM | SM-0001 hazard identification
Mark every assumption unattached and start counting them from day one | SMS Safety Assurance | SM-0001 safety performance monitoring
Separately flag assumptions about people rather than hardware, because nothing in a parts comparison will surface them | Human Factors | Assumption register
Put the cost of discharging these assumptions into the bid rather than discovering it later | Program Management | Basis of estimate
Name the assumption register in the configuration management plan and give it an identifier convention | Configuration Mgmt | CM plan
This is the state where the work is cheapest and where we currently do none of it.

## Slide 20
FIRST HAZARD ANALYSIS, FIRST REAL SCOPING DECISION
State 1 · Concept and early design
The first system-level hazard analysis is where we find out which assumptions are actually load-bearing. This is also where the tiering decision gets made, and where inherited risk acceptance has to be replaced with a decision made on this program.
Action required | Who owns it | Hangs off
Run system-level hazard identification and test each assumption against it: does it close or reduce a hazard, or not? | SRM | SM-0001 hazard identification
Make the tiering decision. Only assumptions carrying safety risk credit go into full control | SRM with SMS | Tiering criteria
Assign a named risk acceptor on this program to every Tier 1 assumption. Inherited acceptance does not carry over | SMS, Accountable Executive delegate | SM-0001 risk acceptance
Document the organizational system description, which sets the outer boundary of what is in scope | SMS | SM-0001 system description
Attach operating-environment and performance assumptions to the approved system specification | Systems Engineering | Functional baseline
Nominate the top-level safety-significant items for individual tracking and agree them with the customer | Configuration Mgmt with Systems Eng | EIA-649-1 item selection
Set the assumption register up as a controlled data type in the release system | Configuration Mgmt | CM plan
If the tiering decision is made well here, everything downstream stays affordable. If it is made badly, the practice will be abandoned within a year.

## Slide 21
WHERE INHERITED ASSUMPTIONS MOST OFTEN FAIL
State 2 · Development and subsystem design
Most assumptions that go wrong are about the item's surroundings rather than the item: what it is bolted to, what it talks to, how hot it gets, who maintains it. This is the state where those become attachable, and it is the highest-yield state in the whole sequence.
Action required | Who owns it | Hangs off
Push hazard analysis down to subsystem level and restate assumption conditions at that level | SRM | SM-0001 hazard identification
Attach interface, installation, thermal, loads and duty-cycle assumptions to the subsystem requirement documents | Systems Engineering | Allocated baseline
Identify all internal and external interface requirements, write them into the controlled documentation and place them under change control | Configuration Mgmt | EIA-649-1 interface control
Nominate lower-tier safety-significant items; each one pulls its dependent assumptions into scope | Configuration Mgmt with Systems Eng | EIA-649-1 item selection
Attach human-factors assumptions to procedure, training and manual documents rather than to hardware | Human Factors | Procedural baselines
Start reporting the count of unattached Tier 1 assumptions against agreed review criteria | SMS Safety Assurance | Design review criteria
Flow assumption ownership and reporting duties to suppliers through contracts and interface agreements | Supply Chain with Config Mgmt | SM-0001 interfaces
In the running example, three of the four broken conditions become visible at this state if anyone is looking for them.

## Slide 22
THE FIRST POINT AT WHICH SIMILARITY CAN BE CHECKED RATHER THAN ASSERTED
State 3 · Detail design through critical design review
This is the gate. Until now, "the hardware is the same" has been an assertion. Here there is enough detailed definition on both sides to actually compare them. It is also the last comfortable moment to find out that an inherited assumption does not hold.
Action required | Who owns it | Hangs off
Attach remaining assumptions to specific items at specific revisions, citing the document rather than repeating its contents | Systems Eng with Config Mgmt | Product definition
For every inherited assumption, run a written comparison of source and receiving program covering each condition, not just the part number | Systems Eng with SRM | Assumption register
Any condition that cannot be verified against this program's own data goes back into safety risk management rather than transferring | SRM | SM-0001 risk management
Assess risk against the defined acceptability criteria. Raise any Tier 1 assumption still lacking a named acceptor as a finding | SMS | SM-0001 risk acceptance
Add a field to the engineering change proposal form asking which assumptions the change affects | Configuration Mgmt | ECP form and process
Confirm the status accounting system can answer: which assumptions depend on this item at this revision? | Configuration Mgmt | Status accounting
Check operator and maintainer assumptions against the actual draft procedures and task analysis | Human Factors | Task analysis
Hold the review criterion: unattached Tier 1 assumption count at or below the agreed threshold | Program Management | Design review criteria
If only one thing from this deck is adopted, make it the comparison in row two and the form field in row five.

## Slide 23
EVIDENCE REPLACES ASSERTION
State 4 · Verification, audits and certification
Assumptions that have survived this far now get tested. Where an assumption turns out to be wrong, it stops being an analysis issue and becomes a change with cost and schedule consequences, which is why the earlier states matter so much.
Action required | Who owns it | Hangs off
Move assumptions from attached to verified as test, analysis and audit evidence accumulates | Systems Engineering | Assumption register
Extend requirement-to-test traceability back to the assumption that scoped the requirement | Systems Eng with Quality | Verification traceability
Handle any assumption falsified by test as a major change, because it affects safety | Configuration Mgmt | EIA-649-1 change classification
Complete the functional and physical configuration audits and reconcile production against development definition | Config Mgmt with Quality | EIA-649-1 audits
Validate the risk controls that depended on assumptions and confirm effectiveness measures exist | SRM with SMS | SM-0001 safety assurance
Confirm assumed task times, alerting detection and workload by test or simulation rather than by assertion | Human Factors | Human factors validation
In the running example, this is where the different alerting threshold would surface, at roughly a hundred times the cost of catching it at proposal.

## Slide 24
KEEPING THE LINK ALIVE ONCE CHANGE VOLUME INCREASES
State 5 · Production
Production is where the largest number of changes happen and where the discipline is most likely to quietly lapse. The controls here are mostly about making sure the mechanism keeps running rather than about new analysis.
Action required | Who owns it | Hangs off
Screen every engineering change proposal for effect on assumptions | Configuration Mgmt | ECP process
When a repeated deviation is made permanent, reopen the assumptions it touches | Config Mgmt with SRM | EIA-649-1 variance handling
Monitor whether assumption re-checks are actually being done on change, or quietly waived | SMS Safety Assurance | SM-0001 change management assurance
Maintain status accounting by item and reconcile as-designed against as-built | Configuration Mgmt | Status accounting
Treat repeated nonconformances as candidate invalid manufacturing or human-factors assumptions | Quality with Human Factors | SM-0001 hazard identification
Trigger a human-factors assumption review when a procedure or training course is revised, even though no hardware change exists | Human Factors with Config Mgmt | Procedural baselines
The last row closes a real gap: procedure and training changes generate no hardware change record, so today nothing prompts a re-check.

## Slide 25
THE LOOP CLOSES, THEN IMMEDIATELY REOPENS
State 6 · In service, and handing on to the next program
Field evidence is the only thing that can test assumptions about how the aircraft is actually operated and maintained. It is also the state where this program becomes the source that the next program borrows from, which is where the whole cycle either improves or repeats.
Action required | Who owns it | Hangs off
Route continued operational safety findings to assumption owners, not only to hazard owners | SRM | SM-0001 safety assurance
Re-check assumptions on a schedule and on trigger, and track how long since each was last confirmed | SMS Safety Assurance | SM-0001 continuous improvement
Confirm that retrofit and modification embodiment matches the configuration the assumption relied on | Configuration Mgmt | Status accounting
Use configuration history to work out which aircraft a falsified assumption actually applies to | Configuration Mgmt | Status accounting
When exporting to a derivative or new program, send the conditions, the document references and the verification evidence with the statement | Program Mgmt with Systems Eng | Assumption register
Do not release bare assumption statements to another program. That is precisely what created this problem | SMS | Enterprise policy
A program that exports well makes the next program cheaper. A program that exports badly makes it more dangerous.

## Slide 26
OWNERSHIP SUMMARY
Who owns what, across the whole lifecycle
No single activity owns this end to end today, which is the underlying reason it falls through. The proposal spreads specific duties across six activities and asks the safety organization to hold the overall position.
Program Management
Funds and schedules the work. Owns the design review criteria and the reported position on unattached assumptions. Owns what gets exported to the next program.
Systems Engineering
Writes the conditions. Performs the attachment to documents and the source-to-receiving comparison. Owns the citation rather than the restatement.
Configuration Management
Makes the register a controlled data type, maintains the link to items and documents, adds the field to the change form, and provides the query that finds affected assumptions.
Safety Risk Management
Decides which assumptions carry risk credit, reopens the ones that cannot be verified, and routes in-service findings back to assumption owners.
SMS Safety Assurance
Owns scope through the system description, the named-acceptor rule, the monitoring of whether re-checks actually happen, and periodic re-validation.
Human Factors
Owns the class of assumptions that have no part number. Attaches them to procedure and training documents and validates the claims about people by test rather than assertion.
Quality and Supply Chain carry supporting actions in States 2, 4 and 5. The single accountable position sits with the Safety Accountable Executive, because that is the only role with authority over both the cost pressure and the risk it creates.

## Slide 27
BEYOND HARDWARE · HUMAN FACTORS
Assumptions about people, which no parts comparison will ever find
A similarity review compares hardware. Assumptions about people have no part number, so nothing in that comparison surfaces them. They are simultaneously the most frequently reused assumptions we hold and the least frequently checked.
Typical examples: assumed crew training standard and recency · assumed workload during the phase of flight in question · assumed maintainer skill level and certification · assumed probability that an inspector will spot a defect · assumed time available to complete a procedure · assumed alerting salience · assumed staffing levels · assumed shift patterns and fatigue exposure · assumed compliance with the written procedure
Where their validity actually lives
Not in drawings. In the operating environment: people, procedures, facilities, training. SM-0001 already treats all of that as part of the organizational system description, so the concept is available to us.
What to attach them to
Procedure documents, training curricula, task analyses and the maintenance manual. Where these carry safety risk credit, they need the same change control as a drawing, because that is what makes the trigger work.
The gap that lets them rot
A procedure revision or a training course update generates no engineering change against hardware. Nothing in the current system prompts anyone to ask whether an assumption just broke. This has to be an explicit trigger in its own right.
The disguised case worth calling out
Detectability ratings in a failure modes analysis are assumptions about human performance wearing hardware clothing. So are assumed inspection intervals. Reuse those and you have silently reused another program's workforce and maintenance organization.
SM-0001 already requires risk controls to take operational, technical, human and organizational factors into account. This is not an extension of the standard, it is an application of it.

## Slide 28
BEYOND HARDWARE · INTERFACES
Same box, different everything it touches
Reuse by similarity is a claim about the item. An interface assumption is a claim about the item's surroundings, which is exactly what did not come across. This is where inherited assumptions fail most often.
Technical interfaces · between parts of the product
The obligation already exists. Internal and external interface requirements have to be identified, written into the controlled documentation and kept under change control, with a representative on the interface working group where one exists. Attaching interface assumptions to those documents adds a link, not a process.
Organizational interfaces · between companies
The classic failure: the supplier assumed the integrator was covering it, and the integrator assumed the supplier had. The assumption falls into the gap between two safety management systems, each of which believes the other owns it. The fix is to name an assumption owner for each interface in the interface documentation.
One caution on how the interface provisions get read
SM-0001 deliberately limits how much hazard and risk analysis has to be pushed across an organizational boundary; knowing that a risk is being assessed and controlled by the responsible party is often enough. That should not be read as permission to withhold interface assumptions. The assumptions that cross a boundary are the minimum necessary exchange, because each side is relying on them and neither can see the other's. They are the content that provision exists to protect, not to suppress.
In the running example, three of the four broken conditions are interface conditions: the alerting logic, the maintenance program and the bay layout. The hardware really was identical.

## Slide 29
PULLING IT TOGETHER
Three kinds of assumption, three things to attach them to
The mechanism is the same in each case. What differs is which controlled document the assumption points at, and therefore which change process raises the flag when something moves.
Hardware and performance
POINTS AT
Configuration items and the approved product definition
Systems Engineering with Configuration Management
Attaches during subsystem design, firms up at critical design review, verified at the configuration audits.
People and organization
POINTS AT
System description, plus procedure, training and manual documents
Human Factors with SMS
Attaches during subsystem design, and must be re-checked on every procedure or training revision.
Interfaces
POINTS AT
Interface control documentation, interface agreements and contracts
Configuration Management with Supply Chain
Attaches during subsystem design, with a named assumption owner recorded for each interface.
An assumption that points at none of these three is not an assumption. It is a hope with a document number.

## Slide 30
WHAT I AM ASKING FOR
Five decisions
1
Name the assumption register in the configuration management plan
Give it an identifier convention, a control class and a place in the release system. Configuration Management owns the mechanism. Nothing else works until this exists.
2
Require a named risk acceptor on this program for every safety-bearing assumption
Inherited acceptance from the source program does not carry over. This is the item with genuine compliance weight, and it is the one to lead with in front of program leadership.
3
Add one field to the engineering change proposal form
Ask which assumptions the change affects. A form change, not a new process, and it converts assumption review from something people must remember into something the workflow asks for.
4
Report the count of unattached safety-bearing assumptions at design reviews
At system, preliminary and critical design review. Program Management owns the position; Safety Assurance owns the measure. Expect the first number to be uncomfortable.
5
Stop releasing bare assumption statements to other programs
The conditions, the document references and the verification evidence travel with the statement, or nothing travels. This is what stops us manufacturing the same problem for the next program.
Two honest caveats: neither SM-0001 nor EIA-649-1 requires an assumption register today, so this is a bridge we are building rather than an existing obligation, and it should be annotated as such. And applied to everything it is unaffordable, so the tiering decision on slide 17 is the thing that determines whether it survives.

## Slide 31
REFERENCE
Glossary
Ground rules and assumptions
Statements a program adopts as true in order to bound analysis and design. In safety work they usually carry risk credit, meaning a hazard was closed partly because of them.
Configuration item
A part of the product designated for individual tracking and change control. Safety-significant items are already required to be designated as such.
Configuration documentation
The approved drawings, specifications and requirements defining what an item is supposed to be.
Baseline
An approved snapshot of that documentation. Functional covers what the system does, allocated what each part does, product what it actually is.
Engineering change proposal
The formal package proposing a change to something baselined, including an assessment of the full extent of its effects.
Configuration status accounting
The record-keeping that can report the current approved definition of an item and what changes are outstanding against it.
Binding or attaching
Used in this deck to mean linking an assumption to the specific controlled document that makes its conditions checkable.
Risk credit
The reduction in assessed risk that an assumption is providing. If the assumption fails, the credit is withdrawn and the hazard reopens.
Standard references used in this deck: SM-0001 Issue C for safety management system and safety risk management requirements; EIA-649-1 and GEIA-HB-649 for configuration management requirements and guidance.