## Slide 1: How Comparator Lines Up Program Data
DATA ALIGNMENT
Core BOM
Supplemental
Loaded after a run
Matches the EBOM line directly
Matches through a work order or NCR
EBOM
Engineering BOM · as designed
one line per Part # + Next Higher
EBOM LINE ITEM
Part # + Next Higher
Is it planned?
Is it built?
Under a closed work order?
In the right quantity?
What changed? What is open?
one result per line
MBOM
Manufacturing BOM · as planned
Part # + Used On
3 passes
ABOM
As-Built BOM · as built
Part # + Used On
3 passes
CHANGE PEDIGREE
DCN · ECN · ECR history
Part # + Next Higher
or Drawing #, set per program
CONFIG ITEMS
the CI list
Part # + Next Higher
ACN
clearance level and record
Part # only
ME ADJ
engineer calls, after a run
Part # → failing position
each row carries its WO #
WORK ORDER # from the ABOM, links records to EBOM lines
WO5
install and remove log
WO # + Part #
NCR
nonconformances
originating WO #
RFV
approved variances
NCR Disp #
WO #
Part # + Next Higher
results per line
WHAT COMES OUT
Coverage %: planned, built, closed
Issue cards and drill-downs
Comparison Summary and reports
Frozen session, audit certificate
Notes: Every result in Comparator belongs to one EBOM line item: a part number under its next higher assembly. MBOM and ABOM decide whether each line is planned and built. Change Pedigree, the CI list, ACN and engineer adjudications attach by part number. WO5, NCR and RFV have no part position of their own, so they reach the line through the work order that built it. Matches are exact; part numbers are compared after trimming spaces and ignoring case.

## Slide 2: Three Checks Behind “Planned” and “Built”
THE RECONCILIATION
MBOM and ABOM are each tested against every EBOM line three ways. A line can pass more than one.
Next Higher
Part
1
PASS 1 · DIRECT
Same part, same parent
The part number sits under the same next higher the design names. Quantity is checked here and only here.
Part
child
child
2
PASS 2 · USED-ON
The part is a parent
Other parts were built into it, so it is present as an assembly. This proves presence, not quantity.
Assembly
Part
3
PASS 3 · ANCESTOR
An assembly above it counts
The part is not listed itself. A higher assembly that contains it is accounted for, up to ten levels up.
ABOM credit needs a closed work order. A part found only under open work orders is flagged WO Not Closed. A part that fails every check, open or closed, is Missing.

## Slide 3: Each Source, What It Brings, How It Lines Up
ALIGNMENT KEYS
SOURCE | WHAT IT BRINGS | HOW IT LINES UP
CORE BOMS |  | 
EBOM | The design baseline | Defines the line: Part # + Next Higher. Duplicate lines merge into one.
MBOM | The build plan | Part # + Used On, in three passes. Used On is the MBOM’s name for next higher.
ABOM | As-built record, WO status, quantities | Part # + Used On, in three passes. Closed work orders earn credit; open ones are flagged.
MATCHED TO THE LINE BY PART NUMBER |  | 
Change Pedigree | DCN, ECN, ECR history; Drawing column | Part # + Next Higher, then part # alone. Drawing + ECR programs use Drawing #, with revision if chosen.
CI list | Which lines are Configuration Items | Part # + Next Higher. Part # alone when the CI has no next higher.
ACN | Clearance level, record number, revision | Part # only. A part used in several places shows the same ACN at each.
ME ADJ | Engineer decisions from another tool | Part #, then the position that is failing. If several fail, an engineer picks one.
MATCHED THROUGH A WORK ORDER OR NCR |  | 
WO5 | Install and remove actions, serials, dates | WO # + Part #, using the work orders the ABOM credited to the line.
NCR | Discrepant parts, dispositions, cause codes | Originating WO #. The ABOM rows on that work order must name the line’s part or its next higher.
RFV | Approved variances | Three routes: Part # + Next Higher; NCR Disp #; or WO # on the MBOM or ABOM.
Matches are exact. Part numbers are compared after trimming spaces and ignoring case. There is no fuzzy matching.