## Slide 1
SAFETY MANAGEMENT · CONFIGURATION MANAGEMENT
Inherited Assumptions: A Gap Between Our Safety and Configuration Systems
Programs reuse ground rules and assumptions from earlier programs when the hardware looks similar. The conditions those assumptions depended on do not come with them, and nothing in our current process notices when they change.
Five decisions requested. Configuration management terms are explained on slide 8, glossary at the back.

## Slide 2
EXECUTIVE SUMMARY
The argument on one page
1. What we do today
A new program reusing hardware from an earlier program also reuses that program's assumptions. The sentence is copied. The conditions that made it true are not.
2. Why that is a safety problem
An assumption is a promise that a risk is acceptable so long as certain things stay true. Without the conditions written down, nobody can tell when it has stopped being true.
3. Why programs do it anyway
Rebuilding assumptions costs senior engineering time in the most schedule-compressed phase. The cost is immediate and visible; the risk is deferred and invisible.
4. Where it shows up as exposure
SM-0001 requires a named person to accept residual risk. Inherited assumptions arrive with nobody named. That is a compliance gap, not just untidy engineering.
The proposal
Configuration management already tracks which engineering documents change and what depends on them. If assumptions point at those documents, a hardware change automatically raises the question of whether the assumption still holds. Today nothing raises that question. We are proposing to connect two systems we already run, not to build a third.
We are not asking programs to slow down or stop reusing. We are asking that reuse leave a trace that can be checked later.

## Slide 3
WHAT WE ARE TALKING ABOUT
An assumption is a conditional promise, not a fact
In safety work an assumption is what lets an analysis stop somewhere. It says a hazard needs no further treatment because something else is taking care of it.
"This hazard is acceptable without additional design mitigation, PROVIDED that the crew is alerted within one flight, the line is inspected every 400 flight hours, and the unit sits outside the icing-exposed bay."
The claim
Short, quotable, and easy to carry to another program. This is the part everyone reads and repeats.
The conditions
Longer, less memorable, and the first thing lost in a copy across. They are what make the claim true.
The risk credit
A hazard was closed without a design change because of this. That is a real safety decision, and someone accepted it.
This is not a new idea
SM-0001 already treats assumptions this way. Appendix 2 lists them among the contents of a hazard record, and the reason given is so they can be re-examined when they change, to check whether the risk assessment still stands. The standard therefore assumes we know when an assumption has changed. For inherited assumptions, we do not.

## Slide 4
WORKED EXAMPLE
A real shape this takes
A pressure sensor is qualified and in service on Program A. Program B is a derivative and reuses the same unit, same part number, same supplier. The assumption set is carried across on that basis.
Program A · what the assumption relied on
Alerting
Crew is alerted to a blocked line within one flight.
Procedure
Dispatch governed by a specific MEL condition.
Inspection
Line inspected every 400 flight hours.
Installation
Unit sits in a heated bay, outside the icing zone.
So
Undetected blockage needs no design mitigation. Hazard closed.
Program B · what is actually different
Alerting
Different avionics supplier, different detection threshold.
Procedure
Different operator, different MEL, rewritten procedure.
Inspection
Customer maintenance program uses 600 flight hours.
Installation
Bay layout changed. Unit now near the icing zone.
So
The part number is identical. Every condition has moved.
Nobody made a mistake. Four teams made four reasonable changes at four different times. No single person ever saw them together next to the assumption they invalidate.

## Slide 5
WHY PROGRAMS REUSE
This is an incentive problem, not a discipline problem
Reuse of assumptions is a rational response to real schedule and cost pressure, and in most cases it produces the right answer. Any proposal that ignores that will be rejected, and should be.
The pressure is real
Assumption sets are written during proposal and early design, the most compressed phase of any program. Rebuilding one costs weeks of senior engineering time the bid does not have.
The incentives point one way
Rebuilding costs the bid, now, visibly. Not rebuilding costs execution or the fleet, years later, invisibly. Every individual decision to reuse is locally sensible.
Reuse is usually correct
When the part, the installation, the environment, the customer and the maintenance program are genuinely the same, the earlier assumption holds and rebuilding it wastes money.
So the problem is not reuse
The problem is reuse in a form nobody can check. If the conditions are not written down and not tied to anything, then when one changes there is no way to find out.
What we are actually asking for
Writing the conditions down at the moment the assumption is made costs minutes, because the engineer making it already knows them. Reconstructing the same conditions three years later costs weeks, and often cannot be done at all. The expensive version of this work is the one we do today.

## Slide 6
WHAT GOES WRONG
The conclusion travels. The conditions stay behind.
What physically moves between programs is the sentence. The reasoning lives in the head of an engineer, in a review held years ago, and in another program's documents.
What arrives
"Undetected blockage needs no design mitigation." One sentence, reviewed and approved, now part of how the new program understands the product.
What stays behind
The alerting threshold, the MEL condition, the inspection interval, the bay location, and the name of whoever accepted the residual risk.
A part number answers only one of these questions
How and where it is installed
How hard it is worked
Temperature, vibration, icing
How often it is inspected
What the crew is alerted to
What it is connected to
How the operator actually flies it
What maintenance requires
A part number is a claim about one box. An assumption is a claim about that box inside a whole aircraft, a whole operation and a whole organization.

## Slide 7
EXPOSURE
Two consequences leadership should care about
1. Risk accepted by nobody
Behind every assumption that closes a hazard there is a person who accepted the residual risk. When the assumption is inherited, that acceptance does not come with it and no equivalent decision is made here.
SM-0001 requires acceptability criteria to be defined and responsibility for accepting risk to be clearly assigned. An inherited assumption still carrying risk credit at critical design review, with nobody named, does not meet that.
2. Cost that compounds by stage
The objection to this work is that it costs time we do not have. That only holds if you compare it against zero rather than against the cost of finding out later.
The cheapest point in the whole lifecycle to capture an assumption is the one point where we currently capture nothing.
Proposal
Write the conditions down while you still know them
Minutes per assumption
Preliminary design
Check against the emerging design
Hours to days, nothing committed yet
Critical design review
Find out it does not hold
Weeks to months, design change and rework
Certification
Find out during compliance demonstration
Months, re-analysis and possible schedule slip
In service
Find out from field evidence
Fleet action, service bulletin, possible AD
Cost shape is illustrative rather than measured across our programs.

## Slide 8
CONFIGURATION MANAGEMENT, IN PLAIN LANGUAGE
The machinery we already have
Configuration management keeps track of what the product is supposed to be, what it actually is, and what changed. It runs on every program today. These are the four terms the rest of this deck uses.
Configuration item
A part of the product important enough to be tracked in its own right, with its own identifier, documents and change control. Not every bracket. The engine controller, yes.
Baseline
An approved snapshot of the drawings, specifications and requirements that define an item at a point in time. After that, changes go through formal review.
Engineering change proposal
The formal package proposing a change to something baselined. It has to describe the full extent of the change's effects before anyone approves it.
Configuration status accounting
The record-keeping that can answer what the current approved definition of an item is, and what changes are outstanding against it. In effect, a searchable index of the product.
Why this matters here
Two things are already true and neither requires a new process. First, the standards already require that items whose failure could cause serious injury or loss of life be designated for individual tracking, so the safety-significant items are already on a maintained list. Second, status accounting is the only system on the program that already knows what changed and what depends on it. Point assumptions at that list, and that system can tell us which assumptions a change puts at risk.

## Slide 9
THE OBVIOUS OBJECTION, ANSWERED
We do not have to wait for the design to mature
Assumptions are written at proposal. Configuration items do not exist for years. But the definition firms up in stages, and each stage gives an assumption something firmer to point at.
Functional baseline
What the system has to do
Operating environment and performance assumptions attach here.
Allocated baseline
What each part has to do
Interface, installation, thermal and duty-cycle assumptions attach. So do most assumptions about people, which attach to procedure and training documents.
Product baseline
What it actually is
Assumptions attach to specific items at specific revisions, and can be verified by test and audit.
Assumptions start unattached at proposal and attach as baselines arrive. What matters is not that they are all attached quickly, but that the number still unattached is visible, reported at design reviews, and falling.
Expect the first number a program reports to be uncomfortable. That is the point of measuring it.

## Slide 10
WHAT WE ARE PROPOSING
The fix, in one page
Write the conditions down when the assumption is made
A short record: what is assumed, why, and specifically what has to be true. Written by the person who knows, when they know it. This is the cheap step that unlocks everything else.
Point each condition at a controlled document
If it depends on a 400-hour inspection interval, cite the document that sets the interval rather than repeating the number. Restating is how assumptions go stale silently.
Give every risk-bearing assumption an owner here
Someone on this program accepts the residual risk. Inherited acceptance does not carry over. This is the item SM-0001 already requires.
Let the change process raise the question automatically
Once assumptions cite controlled documents, a change against one surfaces every assumption depending on it. Nobody has to remember; the mechanism remembers.
Count what is still unattached, and report it
Assumptions attach progressively as baselines arrive. The unattached count becomes a design review criterion.
Do not inherit. Re-adopt.
An assumption cannot cross as-is. It is re-adopted after a documented comparison of the two programs covering the conditions, not the part number. Anything unverifiable goes back into risk management.
Five of these six are record-keeping and routing. Only the last costs real engineering time, and only for the small set of assumptions that actually carry risk credit.

## Slide 11
HOW IT ACTUALLY WORKS
The mechanism, and the cheapest way to switch it on
Restated · goes stale silently
"Assumes the line is inspected every 400 flight hours."
When the maintenance program moves to 600 hours, nothing connects that change to this sentence. It stays in the document, still reading as true, for the life of the program.
Cited · breaks loudly when it should
"Assumes the inspection interval defined in [document, item, revision]."
When that document is revised, the change record shows this assumption among the things affected, and someone has to say whether it still holds.
Why the citation is what makes it work
Under EIA-649-1 an engineering change proposal has to describe the full extent of a change's effects before approval, and safety-affecting changes are classified as major. If assumptions cite controlled documents, they appear inside that assessment automatically. If they restate values, they are invisible to it.
The cheapest intervention in this deck
Add one field to the engineering change proposal form asking which assumptions the change affects. That is a form change, not a new process. It converts assumption review from something people have to remember into something the workflow asks for, on every change, without anyone being trained to do it.

## Slide 12
KEEPING IT AFFORDABLE
Not every assumption gets the same treatment
If this applies to every assumption on a program it will be rejected, and rightly. The scope decision is made once, early, and it determines whether the practice survives contact with a schedule.
TIER 1
Controlled
Assumptions a hazard analysis or certification finding depends on. Full record, cited documents, named risk acceptor, reported at design reviews.
IN PRACTICE
A small minority. On most programs, tens of items rather than hundreds.
TIER 2
Registered
Assumptions that shape design decisions but carry no safety risk credit. Identifier, owner, statement and reasoning only.
IN PRACTICE
Cheap. Its value is that an item can be promoted to Tier 1 later if analysis shows it is load-bearing.
TIER 3
Engineering note
Everything else: working assumptions, estimating conventions, modeling simplifications with no safety consequence.
IN PRACTICE
No control at all. Saying so explicitly is what keeps Tier 1 credible rather than diluted.
Tier 1 scope is bounded by two artifacts we already produce: the organizational system description SM-0001 requires, and the safety-significant item list the configuration item selection process already maintains. That makes the boundary defensible to an auditor without inventing a new rule.

## Slide 13
ACTIONS, PART 1 OF 2
What happens when, and who owns it · early lifecycle
Four states, from bid through critical design review. This is where almost all of the value is, because it is where assumptions are created, scoped and last cheaply checkable.
Lifecycle state | What has to happen | Who owns it
Proposal and pre-award | Write down each safety-bearing assumption with its conditions and reasoning as it is made. Record where an inherited one came from and what the similarity claim rested on. Put the cost of discharging them into the bid. | Systems Engineering Program Management
Concept and early design | First hazard analysis decides which assumptions actually carry risk credit; the rest are tiered out. Name a risk acceptor on this program for each one that does. Inherited acceptance does not carry over. | Safety Risk Management SMS
Development and subsystem design | Attach assumptions to the subsystem and interface documents as those are approved. Attach assumptions about people to procedure and training documents. Begin reporting the count still unattached. | Systems Engineering Human Factors Configuration Management
Detail design through CDR | Compare source and receiving program condition by condition rather than part number to part number. Anything that cannot be verified goes back into risk management. Add the assumption field to the change form. | Systems Engineering Safety Risk Management Configuration Management
If only two things from this deck are adopted, make them the comparison at CDR and the field on the change form.

## Slide 14
ACTIONS, PART 2 OF 2
What happens when, and who owns it · later lifecycle
Three states, from verification into service. The work here is mostly about keeping the mechanism running once change volume rises, and about not exporting the same problem to the next program.
Lifecycle state | What has to happen | Who owns it
Verification, audits and certification | Confirm conditions by test, analysis and audit, and move assumptions to verified. An assumption falsified by test is handled as a major change because it affects safety. Confirm assumed task times and alerting by test rather than assertion. | Systems Engineering Quality Human Factors
Production | Screen every engineering change for effect on assumptions. When a repeated deviation is made permanent, reopen the assumptions it touches. Trigger a review when a procedure or training course is revised, even though no hardware change exists. | Configuration Management Human Factors SMS
In service, and handing on | Field evidence is the only thing that tests assumptions about how the aircraft is actually operated and maintained; route findings to assumption owners. Nothing leaves for the next program without its conditions, references and evidence. | Safety Risk Management SMS Program Management
A program that exports well makes the next program cheaper. A program that exports badly makes it more dangerous.

## Slide 15
BEYOND HARDWARE
Two categories a hardware comparison will never surface
A similarity review compares parts. The assumptions most likely to be wrong are not about parts at all, which is why nothing in the current process catches them.
Assumptions about people
Crew training standard and recency. Workload in the phase of flight concerned. Maintainer skill level. The probability an inspector spots a defect. Time available to complete a procedure. Staffing and fatigue.
These have no part number, so nothing in a parts comparison raises them. Their validity lives in procedures, training and staffing, not in drawings.
The gap: a procedure or training revision generates no engineering change against hardware, so nothing today prompts anyone to ask whether an assumption just broke.
Assumptions about interfaces
Reuse by similarity is a claim about the item. An interface assumption is a claim about the item's surroundings, which is exactly what did not come across.
Technically, the obligation already exists: interface requirements must be identified, documented and change-controlled. Attaching assumptions to them adds a link, not a process.
Organizationally, the classic failure is that the supplier assumed the integrator covered it and the integrator assumed the supplier had. The assumption falls into the gap between two safety management systems.
Why this matters more than the hardware case
In the worked example, three of the four broken conditions are interface or people conditions: the alerting logic, the maintenance program and the crew procedure. The hardware really was identical. That is the pattern, not the exception, and it is why a parts-based similarity argument is not sufficient evidence for carrying an assumption across.

## Slide 16
OWNERSHIP
Who owns what
No single activity owns this end to end today, which is the underlying reason it falls through the cracks. The proposal spreads specific duties across six activities.
Program Management
Funds and schedules the work. Owns the design review criteria and the reported position. Owns what gets exported to the next program.
Systems Engineering
Writes the conditions, attaches them to documents, and performs the source-to-receiving comparison.
Configuration Management
Makes the register a controlled data type, maintains the link to items, adds the field to the change form, and provides the query that finds affected assumptions.
Safety Risk Management
Decides which assumptions carry risk credit, reopens those that cannot be verified, and routes in-service findings to assumption owners.
SMS Safety Assurance
Owns scope through the system description, the named-acceptor rule, and monitoring whether re-checks actually happen.
Human Factors
Owns the assumptions that have no part number, attaches them to procedure and training documents, and validates claims about people by test.
Single accountable position: the Safety Accountable Executive, because that is the only role with authority over both the cost pressure and the risk it creates.

## Slide 17
WHAT I AM ASKING FOR
Five decisions
1
Name the assumption register in the configuration management plan
Give it an identifier convention, a control class and a place in the release system. Configuration Management owns the mechanism. Nothing else works until this exists.
2
Require a named risk acceptor on this program for every safety-bearing assumption
Inherited acceptance does not carry over. This is the item with genuine compliance weight under SM-0001.
3
Add one field to the engineering change proposal form
Ask which assumptions the change affects. A form change, not a new process, and it makes the workflow do the remembering.
4
Report the count of unattached safety-bearing assumptions at design reviews
Program Management owns the position; Safety Assurance owns the measure. Expect the first number to be uncomfortable.
5
Stop releasing bare assumption statements to other programs
The conditions, the document references and the evidence travel with the statement, or nothing travels.
Two honest caveats: neither SM-0001 nor EIA-649-1 requires an assumption register today, so this is a bridge we are building rather than an existing obligation. And applied to everything it is unaffordable, so the tiering decision on slide 12 is what determines whether it survives.

## Slide 18
BACK-UP
Glossary and references
Ground rules and assumptions
Statements a program adopts as true to bound analysis and design. In safety work they usually carry risk credit, meaning a hazard was closed partly because of them.
Risk credit
The reduction in assessed risk an assumption provides. If the assumption fails, the credit is withdrawn and the hazard reopens.
Configuration item
A part of the product designated for individual tracking and change control. Safety-significant items are already required to be designated.
Baseline
An approved snapshot of the documentation defining the product. Functional covers what the system does, allocated what each part does, product what it actually is.
Engineering change proposal
The formal package proposing a change to something baselined, including an assessment of the full extent of its effects.
Configuration status accounting
The record-keeping that reports the current approved definition of an item and what changes are outstanding against it.
References: SM-0001 Issue C for safety management system and safety risk management requirements. EIA-649-1 and GEIA-HB-649 for configuration management requirements and guidance.