## Slide 1
Sixty Barriers
Reliability, Maintainability, System Health and Human Factors requirements that stand between us and catastrophe
The position that these requirements bind only through contract flow-down is making Severity 4 to 5 risk-acceptance decisions by omission, at the wrong altitude in the organization.
60
clause-anchored barriers
36
documented Sev 4-5 events
23
multi-standard anchored
1,900+
documented fatalities
Briefing | [DATE]

## Slide 2
BLUF
Two positions, and which one the standards support
Current problematic position
“These are contractually invoked engineering standards. If a contract does not require a specific clause, we are not obligated to perform it.”
This deck's position
These requirements are SMS-pathway obligations, not contract-pathway preferences. Suspending one is a Severity 4 to 5 risk-acceptance decision, and the standards themselves say so.
The bottom line for leadership
Whether or not a contract calls out GEIA-STD-0009A, JA1011, MIL-STD-1530D, MIL-STD-882E or MIL-STD-1472H, the SMS standard the organization has adopted independently requires the controls those standards implement. Both pathways bind. And every one of those standards states that tailoring is a documented, risk-assessed, approved act rather than a silent omission.

## Slide 3
The Argument Is Already Written Into MIL-STD-882E
Three clauses, quoted in substance, not our framing imposed on the standards
4.1.1 / 4.1.2
Tailoring can only add
Sections 3 and 4 are the minimum mandatory requirements for an acceptable system safety effort for any DoD system. Tasks may be cited to ADD requirements. Tailoring cannot subtract from the floor.
4.2.2 / 4.2.2.2
Each discipline owns its own risk
System safety personnel are not responsible for hazard management in other engineering disciplines. Each discipline obtains its own risk acceptance from the appropriate risk acceptance authority.
4.3.2
The barrier method is an obligation
Hazard identification shall consider the entire life cycle and shall use mishap data and lessons learned from legacy and similar systems. This assessment is not an initiative. It is a requirement.
Two further clauses carry their own slides. 4.3.4 sets a mitigation order of precedence and states that procedures, training and PPE should not be the only control for a catastrophic hazard. 4.3.3.b states that no amount of doctrine, training, warning, caution or PPE moves a mishap probability to eliminated.

## Slide 4
Two Pathways Both Bind the Organization
The contract may be silent. The SMS is not.
Contract pathway
Standards invoked by contract clause, then selectively tailored.
1
Customer selects clauses or tasks
2
Tailoring applied at program level
3
Contractor performs what was invoked
4
Compliance demonstrated to customer
Contingent on contract scope.
SMS pathway
SM-0001 adopted as the basis of the organization's SMS.
1
Org adopts SM-0001 as SMS basis
2
SM-0001 6.2.1 names the hazards
3
Organization must control those hazards
4
R&M activities are those controls
Not contingent on contract scope.
Both pathways converge on the same activities. MIL-STD-882E 4.2.2.2 adds a third obligation: the discipline must obtain its own risk acceptance either way.

## Slide 5
What “Barrier” Means in SMS Language
Not a metaphor. SM-0001's own definition of a risk control.
SM-0001 defines risk control and mitigation as a means to reduce or eliminate the effects of hazards.
1
The hazard it addresses is one SM-0001 explicitly names
in 6.2.1, 6.2.3, 6.3 or 7. That list names FMECA findings, in-service failures, maintenance data, ambiguous manufacturing or maintenance information, work not performed to approved data, and inadequate training, time, rest or experience.
2
Failure of the requirement directly enables that hazard
without other healthy and critical barriers remaining in the path.
3
Documented historical events demonstrate the consequence
of barrier failure at Severity 4 or 5. Thirty-six of the sixty carry a specific investigated event rather than an industry pattern.
Sixty requirements across six standards satisfy all three. They are barriers in SMS terms.

## Slide 6
What Removing a Barrier Actually Means
In SMS terms, not contract terms
With the barrier in place
✓
Named SMS hazard exists in the environment
✓
The requirement operates as a risk control
✓
Detection exists at the critical control point
✓
Risk plots in the acceptable or monitor zone
Without the barrier
✕
Named SMS hazard still exists in the environment
✕
Risk control absent or substantially degraded
✕
Detection missing at the critical control point
✕
Risk plots in the unacceptable zone
Removing a barrier is not an administrative decision. It is a Severity 4 to 5 risk-acceptance decision, made deliberately or by default.

## Slide 7
Who Has Authority to Accept or Remove a Barrier
SM-0001 6.2.2 requires identification of the management personnel who can accept high, serious and medium risk
Accountable Executive / Business CEO or Delegate
Catastrophic and Severe risk acceptance
Executive (e.g. VP) or Delegate
Significant risk acceptance
First-Line Manager or Delegate
Minor and Negligible decisions
Today's situation
Severity 4 to 5 risk-acceptance decisions are effectively being made at the engineering-organization altitude through interpretation of contract scope. By SM-0001 6.2.2 this is the wrong altitude. MIL-STD-882E 4.2.2.2 says the same thing from the other direction: the discipline must obtain its own acceptance from the authority that owns that severity, and it cannot delegate that upward by assumption or sideways to system safety.

## Slide 8
The Decision Being Made, Whether Recognized or Not
When the organization says no contract means no obligation, it makes a decision it does not have authority to make
“We accept the residual Severity 4 to 5 risk of every SMS hazard that the omitted requirements would have controlled. We assert this acceptance as an administrative determination about contract scope.”
1
It accepts risk that the record shows is real.
Alaska 261, JAL123, United 232, MCAS, Kegworth, Turoy, Cougar 91, AF447, CV-22, KC-130T, Aloha 243. Investigated events, not hypotheticals.
2
It accepts that risk at the wrong altitude.
SM-0001 6.2.2 names who may accept Severity 4 to 5. MIL-STD-882E 4.2.2.2 requires the discipline to obtain that acceptance itself. Neither names the engineering organization.
3
It accepts that risk silently.
No signed risk-acceptance memo, no named accountable individual, no SMS record. A contractual silence read as a tailoring choice.

## Slide 9
The Cumulative Weight of Evidence
Why sixty barriers cannot be dismissed as theoretical
60
clause-anchored barriers
Each traced to a named SM-0001 hazard
36
with a specific event anchor
Investigated accidents, not patterns
54
rated Severity 5
Catastrophic outcomes
23
anchored in two or more standards
Independently obligated
1,900+
documented fatalities
Real outcomes, not hypothetical risk
The multi-anchor figure matters more than the total
A barrier obligated independently by the system safety standard, the reliability standard and the structural integrity standard is not one discipline's preference. Twenty-three of the sixty are in that position. Of fourteen standards reviewed, only six carry normative content capable of anchoring anything at all, which means most of this discipline has no contract pathway to tailor away in the first place.

## Slide 10
The Sixty Barriers
Seven functional clusters, anchored across six standards
01-08
Hazard and failure mode identification
MCAS · United 232 · Continental Express 2574
8
09-13
Risk assessment and classification
Alaska 261 · 787 battery · MCAS
5
14-23
Mitigation and design
Alaska 261 · BA 5390 · Kegworth · KC-130T
10
24-31
Verification and test
Kegworth · Cougar 91 · Qantas 32 · United 232
8
32-42
Maintenance program derivation
Alaska 261 · Southwest 1380 · Chalk's 101 · Turøy
11
43-53
In-service monitoring and closed-loop action
Turøy · CV-22 · JAL123 · AF447 · American 191
11
54-60
Governance, tailoring and risk acceptance
Nimrod XV230 · Columbia · Aloha 243
7
Full clause anchors, event anchors and severity ratings are held in the barrier register.

## Slide 11
Focused Example: Alaska 261 (2000)
Bottom-tier mitigation, named as inadequate by the standard's own order of precedence
What happened
The horizontal stabilizer jackscrew acme nut threads wore through from insufficient lubrication. There was no redundancy, no fail-safe, and no indication of wear. The only control was a scheduled maintenance task, and its interval had been progressively extended without reliability evidence.
88 fatalities
Severity 5
Which barriers failed
14
882E 4.3.4 order of precedence: a procedure was the only control for a catastrophic hazard
15
1530D 5.1.3.5.1: single load path requires slow damage growth design
19
1472H 5.9.16.1.2: indication required when an item is out of tolerance
33
JA1011 5.5.2: assess consequence as if no task is currently being done
42
JA1011 5.10.2 and 5.11.1: review the decisions, and interval formulae must be supportable
MIL-STD-882E 4.3.4 states that signage, procedures, training and PPE should not be the only risk reduction for a catastrophic hazard. Alaska 261 is what that clause is protecting against.

## Slide 12
Focused Example: Japan Airlines 123 (1985)
A repair is a design change to a life-limited structure, and must be substantiated as one
What happened
The aft pressure bulkhead was repaired incorrectly after a tailstrike, halving the fatigue life of the splice. The aircraft then flew roughly twelve thousand further cycles. From the day of that repair, the certified fatigue life of the structure was fiction, and no inspection program was derived against the real condition.
520 fatalities
Deadliest single-aircraft accident on record · Severity 5
Which barriers failed
52
1530D 5.2.4: stress and strength analysis is the basis for determining the adequacy of repairs and modifications across the life cycle
52
1530D 5.3.1: major repairs altering structural load paths require a static ultimate load test of the affected component
16
1530D 5.1.4.2: critical part and process classification with traceability
51
1530D 5.4.6: repairs and modifications recorded to maintain configuration control
This barrier had no clause home until MIL-STD-1530D entered the set. Five hundred and twenty fatalities were previously unanchored.

## Slide 13
Focused Examples: Undemonstrated Credit and the Slow Loop
Two patterns that recur across the register
LN-OJF, Turøy (2016) · 13 fatalities
A second-stage planet gear cracked and propagated in a manner the installed monitoring could not detect. Maintenance credit had effectively been taken for a detection capability whose coverage of that failure mode had never been demonstrated.
Barrier 43 · MIL-STD-1530D 5.4.3.2
Detection capability and monitoring intervals shall be determined from sensor and system-level probability of detection, and the methods for establishing that POD shall be approved before the monitoring system is installed. Taking undemonstrated credit is a silent Severity 5 risk acceptance.
United 585 into USAir 427 · 157 fatalities
A latent rudder power control unit failure mode produced the first accident in 1991. The same failure mode produced the second in 1994, killing 132 more. The gap between the two is the measurable cost of a slow feedback loop.
Barriers 08, 47 · JA1011 5.5.1.1 · GEIA-STD-0009A 7.5.1.7
Hidden failure modes shall be separated from evident ones in consequence categorisation, and field failure modes shall be resolved in a timely manner by an integrated team. The requirement to be timely is the requirement that was missed.

## Slide 14
Five Failure Modes Appear Across the Sixty Cases
Recognize them. The next barrier failure will follow one of these.
A
Optimistic classification
A severity, probability, load estimate, design concept or detection coverage is assigned more favourably than the evidence supports, and nothing downstream re-tests it.
MCAS · 787 battery · Turøy · AF447
B
Evidence-free interval
A task, inspection interval or life limit is set or changed without the substantiation the clause requires.
Alaska 261 · Southwest 1380 · Chalk's 101
C
Slow loop
The fleet produces the signal and the organization does not convert it into action before the second event.
UA585 into US427 · Cougar 91 · CV-22 · AF447
D
Bottom-tier mitigation
A catastrophic hazard is controlled solely by a procedure, task, training or warning, when the order of precedence requires elimination or design change first.
Alaska 261 · Aloha 243
E
Undocumented exception
A required activity is omitted without the rationale, risk assessment and approval the standard itself demands, and the acceptance never reaches the authority that owns that severity.
Nimrod XV230 · Columbia · the current dispute
Patterns D and E map onto the organizational dispute rather than onto engineering error, and both are anchored in explicit clause text rather than argued by analogy.

## Slide 15
None of These Standards Permits Silent Omission
Every one allows tailoring. Every one requires it to be documented, risk-assessed and approved.
MIL-STD-882E
4.1.1, 4.1.2
Sections 3 and 4 are the mandatory minimum. Tasks may be cited only to add requirements.
MIL-STD-1530D
6.1, 5.1.1, 4.1.b
Tailored contractual requirements permitted. Exceptions and their rationale, including risk assessments, must be documented in the program plan and approved by the PEO before SRR.
GEIA-STD-0009A
1.3, 4.5.1.1
Tailoring permitted. All normative activities across all four objectives must be considered in preparing the Reliability Program Plan.
MIL-STD-1530D
4.1.e, 4.2
A revised plan and approval are required before modification, before a new mission, and before operating beyond the certified service life.
SAE JA1010
1.3
Tailoring permitted, against a documented customer agreement.
Contractual silence is not a tailoring decision. It is the absence of one, and the standards do not recognize it as an off-ramp.

## Slide 16
The Ask
Three actions. Specific, executable, defensible.
1
Establish SMS policy
State as SMS policy that the requirements underlying the sixty barriers, or documented equivalent controls, shall be performed on all safety-significant products regardless of contract flow-down.
2
Route exceptions correctly
Where a program believes a barrier requirement is not warranted, route the determination through the SMS risk-acceptance process rather than the engineering tailoring process. Output is a signed risk-acceptance memo at the Severity 4 to 5 authority level.
3
Document equivalent controls
Where a barrier is satisfied by an alternative process, record which alternative satisfies which SM-0001 hazard, with what evidence. This protects SMS conformance posture and engineering credibility at audit.
The ask is structural, not adversarial. It does not require a single additional engineering activity to be performed. It requires that the decision not to perform one be made by the person authorized to make it.

## Slide 17
Anticipated Objections, and the Responses
Removing the off-ramps before they are taken
“The contract does not require it.”
True and irrelevant. The SMS binds the organization independently, and MIL-STD-882E 4.2.2.2 requires the discipline to obtain its own risk acceptance either way.
“Safety owns hazard management, not us.”
MIL-STD-882E 4.2.2 says the opposite in terms. System safety personnel are not responsible for hazard management in other engineering disciplines.
“Reliability is a performance requirement, not a safety one.”
It is both. Alaska 261, Turøy and Cougar 91 were reliability failures with catastrophic outcomes. The discipline that owns the failure mode owns the barrier.
“We will just do something equivalent.”
Acceptable. Document the equivalence as an SMS record, naming which alternative satisfies which hazard with what evidence. If you cannot, it is not equivalent.
“It is too expensive without contract reimbursement.”
Then route the cost against risk trade to the authority empowered to accept Severity 4 to 5 risk. Cost is a legitimate input. It does not change the altitude.
“We have never had an event because we omitted this.”
Survivorship bias. Every cited case is an organization that made the same judgement and outlived it for a while.
None of the standard rejoinders survives engagement with the actual framework. The ask remains.

## Slide 18
The Bottom Line
1
The engineering organization is narrowly correct that these standards are contractually invoked.
2
But contractual silence is not SMS permission, and MIL-STD-882E 4.1.2 says tailoring can only add to the mandatory floor, never subtract from it.
3
Sixty barriers, each tied to a named SM-0001 hazard, sit in requirements across six standards. Twenty-three are obligated by more than one of them.
4
Roughly 1,900 documented fatalities across the cited events. The evidence is investigative-record grade, not theoretical.
5
Severity 4 to 5 risk-acceptance decisions are today being made at the wrong altitude, and MIL-STD-882E 4.2.2.2 places that obligation on the discipline itself.
6
SM-0001 6.2.2 and the organization's SMS command media specify who holds the authority. It is not engineering. It is not contracts.
7
The ask is structural. Establish SMS policy, route exceptions correctly, document equivalents.
The frame proposed here is more complete, more defensible, and more honest about the safety decisions actually being made.