## Slide 1
Reading the traceability (TR) diagrams
Each block names a part; the codes and the verbatim part note text sit beside it. Arrows run up the product tree to the end item. Every example slide is self-contained.
Detail / physical item
End item
Installation drawing
solid border
heavy border + gray fill
dashed border — not a physical part
Codes used in these examples
SER Serialization recording — identifies a single unit.
LOT Lot/batch recording — identifies a manufacturing lot/batch.
TR Traceability records — parent-child links to the end item.
IUID Unique item identifier, reported to the DoD registry.
LL Life-limited — states the limit; adds no record.
CSI Critical Safety Item designation.
FC Fracture-Critical Item designation.
Governing rule (§6.4.1): when an item holds SER or LOT, serialization and traceability records are maintained up the product tree to the end item. LL, CSI, and FC identify a condition — they do not create records on their own and do not cascade.

## Slide 2
Example 1 — Life-limited detail, cycle/usage-controlled
§6.6.1 — remaining life is a per-unit quantity, so the item is serialized. The cascade to the end item begins at its parent.
Higher-level physical parent
SER – SERIALIZATION RECORDING REQUIRED.
TR – TRACEABILITY RECORDS REQUIRED.
Turbine disk (detail part)
LL – LIFE LIMITED PART. THIS PART IS CYCLE/USAGE-CONTROLLED AND IS LIMITED TO A SPECIFIC NUMBER OF USAGES. [NUMBER OF FLIGHTS, CYCLE LIMIT, ETC.].
SER – SERIALIZATION RECORDING REQUIRED. THIS ITEM IS SERIALIZED AND TRACEABILITY MUST BE MAINTAINED BETWEEN THIS ITEM AND ALL HIGHER-LEVEL PHYSICAL ITEMS UP TO THE END ITEM.
Also: landing gear assemblies, shock struts, actuator ballscrews, compressor disks, blades. Each higher physical parent repeats SER + TR up to the end item, which carries the TR terminator note.

## Slide 3
Example 2 — Life-limited detail, age/shelf-life-controlled
§6.6.2 — the limit attaches to the manufacturing lot/batch, so the item is lot/batch recorded and its parent is serialized.
Higher-level physical parent
SER – SERIALIZATION RECORDING REQUIRED.
TR – TRACEABILITY RECORDS REQUIRED.
O-ring / sealant / prepreg
LL – LIFE LIMITED PART. THIS PART IS AGE/SHELF-LIFE-CONTROLLED IRRESPECTIVE OF HOW MANY TIMES IT IS USED. [SHELF LIFE, CURE DATE LIMIT, OR STORAGE AGE LIMIT].
LOT – LOT/BATCH RECORDING REQUIRED. THIS ITEM REQUIRES LOT/BATCH TRACEABILITY AND TRACEABILITY MUST BE MAINTAINED BETWEEN THIS ITEM AND ALL HIGHER-LEVEL PHYSICAL ITEMS UP TO THE END ITEM.
A lot number alone cannot fix location, so the parent is serialized (SER + TR). Contrast §6.6.2's other pairing: a calendar-limited discrete part carrying an ALS entry takes LL + SER, per 14 CFR 45.15(c).

## Slide 4
Example 3 — Serialized detail cascading to the end item
§6.4.1 — a serialized item's physical parents are serialized too, up to the end item.
End item (aircraft tail no.)
TR – TRACEABILITY BEYOND THIS LEVEL IS NOT REQUIRED.
Next assembly (physical parent)
SER – SERIALIZATION RECORDING REQUIRED.
TR – TRACEABILITY RECORDS REQUIRED.
Actuator (serialized detail)
SER – SERIALIZATION RECORDING REQUIRED. THIS ITEM IS SERIALIZED AND TRACEABILITY MUST BE MAINTAINED BETWEEN THIS ITEM AND ALL HIGHER-LEVEL PHYSICAL ITEMS UP TO THE END ITEM.
The leaf holds its own serialization requirement (full SER note). Each physical parent below the end item takes the short SER + TR notes. The end item takes the TR terminator note and receives no SER.

## Slide 5
Example 4 — Lot/batch detail under a serialized parent
§6.3.2 + §6.4.1 — a lot number alone can't establish location, so the parent of a LOT item is serialized.
End item
TR – TRACEABILITY BEYOND THIS LEVEL IS NOT REQUIRED.
Assembly (physical parent)
SER – SERIALIZATION RECORDING REQUIRED.
TR – TRACEABILITY RECORDS REQUIRED.
Bar stock / bulk sealant callout
LOT – LOT/BATCH RECORDING REQUIRED.
A raw-material callout takes the short LOT note text (§6.3.2). The chain of serialized parents then continues up to the end item under §6.4.1.

## Slide 6
Example 5 — One parent over a SER branch and a LOT branch
§6.2.2 + §6.4.1 — TR appears on any node that has children holding SER or LOT.
End item
Parent assembly
Subassembly (serialized)
Bracket (lot-recorded)
TR – TRACEABILITY BEYOND THIS LEVEL IS NOT REQUIRED.
SER – SERIALIZATION RECORDING REQUIRED.
TR – TRACEABILITY RECORDS REQUIRED.
Subassembly — own SER, and TR because it has a lot-recorded child:
SER – SERIALIZATION RECORDING REQUIRED. THIS ITEM IS SERIALIZED AND TRACEABILITY MUST BE MAINTAINED BETWEEN THIS ITEM AND ALL HIGHER-LEVEL PHYSICAL ITEMS UP TO THE END ITEM.
TR – TRACEABILITY RECORDS REQUIRED.
Bracket — lot/batch recorded detail part:
LOT – LOT/BATCH RECORDING REQUIRED. THIS ITEM REQUIRES LOT/BATCH TRACEABILITY AND TRACEABILITY MUST BE MAINTAINED BETWEEN THIS ITEM AND ALL HIGHER-LEVEL PHYSICAL ITEMS UP TO THE END ITEM.
A physical parent ends up SER + TR whether the SER is its own requirement or assigned by the cascade. Both branches trace up to the end item under §6.4.1.

## Slide 7
Example 6 — Installation drawing in the path
§6.4.2 — an installation drawing depicts installation, is not consumed as a physical part, and takes TR only (no SER).
End item
TR – TRACEABILITY BEYOND THIS LEVEL IS NOT REQUIRED.
Installation drawing
TR – TRACEABILITY RECORDS REQUIRED. THIS INSTALLATION DRAWING DEPICTS TRACEABLE PARTS WHOSE SERIAL NUMBERS MUST BE TRACED TO ALL HIGHER-LEVEL PHYSICAL ITEMS UP TO THE END ITEM.
Serialized item (traceable part)
SER – SERIALIZATION RECORDING REQUIRED. THIS ITEM IS SERIALIZED AND TRACEABILITY MUST BE MAINTAINED BETWEEN THIS ITEM AND ALL HIGHER-LEVEL PHYSICAL ITEMS UP TO THE END ITEM.
The installation drawing is the exception to the SER + TR rule for parents: it takes the TR installation note and no SER. Physical parents on either side still cascade normally.

## Slide 8
Example 7 — IUID item and its parent item
§6.5.4 — IUID + SER on the item; SER + TR cascade up, but IUID does not flow up on its own.
End item
TR – TRACEABILITY BEYOND THIS LEVEL IS NOT REQUIRED.
Apply IUID to the end item only if the contract requires it.
Higher physical parent
SER – SERIALIZATION RECORDING REQUIRED.
TR – TRACEABILITY RECORDS REQUIRED.
Parent item (embeds a UII)
IUID – ITEM UNIQUE IDENTIFICATION REQUIRED. THIS ITEM IS A PARENT ITEM. MARK THIS ITEM WITH A UNIQUE ITEM IDENTIFIER (UII) IN ACCORDANCE WITH MIL-STD-130 AND REPORT THE UIIS OF ITS EMBEDDED ITEMS IN ACCORDANCE WITH DFARS 252.211-7003.
SER – SERIALIZATION RECORDING REQUIRED.
TR – TRACEABILITY RECORDS REQUIRED.
DoD serially managed item
IUID – ITEM UNIQUE IDENTIFICATION REQUIRED. MARK THIS ITEM WITH A UNIQUE ITEM IDENTIFIER (UII) IN ACCORDANCE WITH MIL-STD-130 AND REPORT THE UII IN ACCORDANCE WITH DFARS 252.211-7003.
SER – SERIALIZATION RECORDING REQUIRED. THIS ITEM IS SERIALIZED AND TRACEABILITY MUST BE MAINTAINED BETWEEN THIS ITEM AND ALL HIGHER-LEVEL PHYSICAL ITEMS UP TO THE END ITEM.
Apply IUID only to items that hold an IUID requirement and to the parent items the contract identifies. SER and TR are what cascade to the end item.

## Slide 9
Example 8 — Critical Safety Item (CSI)
§6.7.1 — CSI + SER + LOT + IUID on the item; CSI does not cascade; SER + TR do.
End item
TR – TRACEABILITY BEYOND THIS LEVEL IS NOT REQUIRED.
Physical parent
SER – SERIALIZATION RECORDING REQUIRED.
TR – TRACEABILITY RECORDS REQUIRED.
Add IUID here if the contract identifies this as a parent item.
Critical Safety Item
CSI – CRITICAL SAFETY ITEM.
SER – SERIALIZATION RECORDING REQUIRED. THIS ITEM IS SERIALIZED AND TRACEABILITY MUST BE MAINTAINED BETWEEN THIS ITEM AND ALL HIGHER-LEVEL PHYSICAL ITEMS UP TO THE END ITEM.
LOT – LOT/BATCH RECORDING REQUIRED. THIS ITEM REQUIRES LOT/BATCH TRACEABILITY AND TRACEABILITY MUST BE MAINTAINED BETWEEN THIS ITEM AND ALL HIGHER-LEVEL PHYSICAL ITEMS UP TO THE END ITEM.
IUID – ITEM UNIQUE IDENTIFICATION REQUIRED. MARK THIS ITEM WITH A UNIQUE ITEM IDENTIFIER (UII) IN ACCORDANCE WITH MIL-STD-130 AND REPORT THE UII IN ACCORDANCE WITH DFARS 252.211-7003.
CSI marks the condition and stays on the item. Serialization reaches a CSI through IUID (§6.7.1). SER + TR cascade to the end item; IUID applies to the item and to contract-identified parent items.

## Slide 10
Example 9 — Fracture-Critical Traceable Part
§6.7.2 — a safety-of-flight structural component that is single load path or sized by durability/damage tolerance. Takes FC + SER + LOT.
End item
TR – TRACEABILITY BEYOND THIS LEVEL IS NOT REQUIRED.
Physical parent
SER – SERIALIZATION RECORDING REQUIRED.
TR – TRACEABILITY RECORDS REQUIRED.
Fracture-Critical Traceable Part
FC – FRACTURE-CRITICAL ITEM.
SER – SERIALIZATION RECORDING REQUIRED. THIS ITEM IS SERIALIZED AND TRACEABILITY MUST BE MAINTAINED BETWEEN THIS ITEM AND ALL HIGHER-LEVEL PHYSICAL ITEMS UP TO THE END ITEM.
LOT – LOT/BATCH RECORDING REQUIRED. THIS ITEM REQUIRES LOT/BATCH TRACEABILITY AND TRACEABILITY MUST BE MAINTAINED BETWEEN THIS ITEM AND ALL HIGHER-LEVEL PHYSICAL ITEMS UP TO THE END ITEM.
FC marks the condition and does not cascade; SER + TR cascade up to the end item. Contrast Example 10: a Fracture-Critical Part (not traceable) is a separate category that takes LOT only.

## Slide 11
Example 10 — Fracture-Critical Part (not traceable)
§6.7.2 — a separate category: not single load path, not sized by durability/damage tolerance. No FC code, no SER on this basis — LOT only.
End item
TR – TRACEABILITY BEYOND THIS LEVEL IS NOT REQUIRED.
Physical parent
SER – SERIALIZATION RECORDING REQUIRED.
TR – TRACEABILITY RECORDS REQUIRED.
Fracture-Critical Part
LOT – LOT/BATCH RECORDING REQUIRED. THIS ITEM REQUIRES LOT/BATCH TRACEABILITY AND TRACEABILITY MUST BE MAINTAINED BETWEEN THIS ITEM AND ALL HIGHER-LEVEL PHYSICAL ITEMS UP TO THE END ITEM.
The part carries lot/batch recording only for material and process traceability. Its serialized parent still cascades SER + TR to the end item because the LOT child triggers §6.4.1.